Philippine Bidding Documents

(As Harmonized with Development Partners)

Procurement of REPAIR OF PASSENGER TERMINAL BUILDING OF PORT OF ESTANCIA, ILOILO

Government of the Republic of the Philippines

Fifth Edition

August 2016

Preface

These Philippine Bidding Documents (PBDs) for the procurement of Infrastructure Projects (hereinafter referred to also as the “Works”) through Competitive Bidding have been prepared by the Government of the Philippines (GoP) for use by all branches, agencies, departments, bureaus, offices, or instrumentalities of the Government, including government-owned and/or -controlled corporations (GOCCs), government financial institutions (GFIs), state universities and colleges (SUCs), local government units (LGUs), and autonomous regional government.  The procedures and practices presented in this document have been developed through broad experience, and are for mandatory use in projects that are financed in whole or in part by the GoP or any foreign government/foreign or international financing institution in accordance with the provisions of the 2016 Revised Implementing Rules and Regulations (IRR) of Republic Act No. 9184 (R. A. 9184).

This PBDs is intended as a model for admeasurements (unit prices or unit rates in a bill of quantities) types of contract, which are the most common in Works contracting.

The Bidding Documents shall clearly and adequately define, among others: (a) the objectives, scope, and expected outputs and/or results of the proposed contract; (b) the eligibility requirements of Bidders; (c) the expected contract duration; and (d) the obligations, duties, and/or functions of the winning bidder.

In order to simplify the preparation of the Bidding Documents for each procurement, the PBDs groups the provisions that are intended to be used unchanged in Section II. Instruction to Bidders (ITB) and in Section IV. General Conditions of Contract (GCC).  Data and provisions specific to each procurement and contract should be included in Section III. Bid Data Sheet (BDS); Section V. Special Conditions of Contract (SCC); Section VI. Specifications; Section VII Drawings; Section VIII. Bill of Quantities; and Section X. Foreign-Assisted Projects.  The forms to be used are provided in Section IX. Bidding Forms.

Care should be taken to check the relevance of the provisions of the Bidding Documents against the requirements of the specific Works to be procured.  In addition, each section is prepared with notes intended only as information for the Procuring Entity or the person drafting the Bidding Documents.  They shall not be included in the final documents, except for the notes introducing Section IX. Bidding Forms, where the information is useful for the Bidder.  The following general directions should be observed when using the documents:

- All the documents listed in the Table of Contents are normally required for the procurement of Infrastructure Project.  However, they should be adapted as necessary to the circumstances of the particular Project.

- Specific details, such as the “name of the Procuring Entity” and “address for proposal submission,” should be furnished in the BDS and SCC.  The final documents should contain neither blank spaces nor options.

- This Preface and the footnotes or notes in italics included in the Invitation to Bid, BDS, SCC, Specifications, Drawings, and Bill of Quantities are not part of the text of the final document, although they contain instructions that the Procuring Entity should strictly follow.  The Bidding Documents should contain no footnotes except Section IX. Bidding Forms since these provide important guidance to Bidders.

- The cover should be modified as required to identify the Bidding Documents as to the names of the Project, Contract, and Procuring Entity, in addition to date of issue.

- If modifications must be made to bidding procedures, they can be presented in the BDS. Modifications for specific Project or Contract details should be provided in the SCC as amendments to the Conditions of Contract.  For easy completion, whenever reference has to be made to specific clauses in the BDS or SCC these terms shall be printed in bold type face on Section II. Instructions to Bidders, and Section IV. General Conditions of Contract, respectively.

TABLE OF CONTENTS

Section I. Invitation to Bid 	6

Section II. Instructions to Bidders 	10

Section III. Bid Data Sheet 	40

Section IV. General Conditions of Contract 	46

Section V. Special Conditions of Contract 	79

Section VI. Specifications 	83

Section VII. Drawings 	96.

Section VIII. Bill of Quantities 	100

Section IX. Bidding Forms 	103

Section X. Foreign-Assisted Projects 	104.

# Section I. Invitation to Bid

Notes on the Invitation to Bid The Invitation to Bid provides information that enables potential Bidders to decide whether to participate in the procurement at hand. The Invitation to Bid shall be: (a) Posted continuously in the Philippine Government Electronic Procurement System (PhilGEPS) website and the website of the Procuring Entity concerned, if available, and the website prescribed by the foreign government/foreign or international financing institution, if applicable, for seven (7) calendar days starting on the date of advertisement; and (b) Posted at any conspicuous place reserved for this purpose in the premises of the Procuring Entity concerned for seven (7) calendar days, as certified by the head of the Bids and Awards Committee (BAC) Secretariat of the Procuring Entity concerned. (c) Advertised at least once in a newspaper of general nationwide circulation which has been regularly published for at least two (2) years before the date of issue of the advertisement, subject to Sections 21.2.1(c) of the 2016 Revised IRR of R.A. 9184; Apart from the essential items listed in the Bidding Documents, the Invitation to Bid should also indicate the following: The date of availability of the Bidding Documents, which shall be from the time the Invitation to Bid is first advertised/posted until the deadline for the submission and receipt of bids. The place where the Bidding Documents may be acquired or the website where it may be downloaded. The deadline for the submission and receipt of bids from the last day of posting of the Invitation to Bid; and Any important bid evaluation criteria. The Invitation to Bid should be incorporated into the Bidding Documents. The information contained in the Invitation to Bid must conform to the Bidding Documents and in particular to the relevant information in the BDS. For foreign-assisted projects, the Invitation to Bid to be used is provided in Section X-Foreign-Assisted Projects.

Invitation to Bid for

Repair of Passenger Terminal Building of Port of Estancia, Iloilo

- The Philippine Ports Authority, PMO-Panay/Guimaras, through the PPA Corporate Fund (R/M 2017) intends to apply the sum of Five Million, Nine Hundred Forty Six Thousand, Two Hundred Two Pesos and 93/100 (P5, 946, 202.93) being the Approved Budget for the Contract (ABC) to payments under the contract for “Repair of Passenger Terminal Building of Port of Estancia, Iloilo” (A170123).  Bids received in excess of the ABC shall be automatically rejected at bid opening.

The Philippine Ports Authority, PMO-Panay/Guimaras now invites bids for:

Removal of Vinyl Floor Tiles Supply, Deliver and Install Floor Tiles (Ground Floor) Supply, Deliver and Install Floor Tiles ( 2nd Floor ) Supply, Deliver and Install Floor Tiles (Stair). Remove & dispose of old wooden partition to designated area directed by engineer. Fabrication of wooden Partition and installation of glass partition incdg. finishing Surface Preparation, Prime and Final Painting of Doors & Item 4.02. Removal and dispose of existing ceiling incdg stockpiling to designated area. Supply, Deliver and Install of Ceiling including joist and boards (Ground & 2nd Floor) Remove & dispose of old doors & windows to designated site. Supply/Deliver and Install new set of Doors(10sets) and Windows(27sets) Leveling / Finishing of Windows / Door Sill Painting of Doors Paintings of Concrete Walls (Interior & Exterior),Parapet wall, wooden Partitions, trusses and misc.roofings accessories Removal and Disposal of old Corr.G.I Sheets and other accessories Supply, Deliver and Install of new Roofing and accessories. Fixtures and Receptacles Power Panels & Service Equipment

- Completion of the Works is required 210 Calendar Days from the effective date of the contract. Bidders should have completed a contract similar to the Project. The description of an eligible bidder is contained in the Bidding Documents, particularly, in Section II. Instructions to Bidders.

- Bidding will be conducted through open competitive bidding procedures using non-discretionary “pass/fail” criterion as specified in the 2016 Revised Implementing Rules and Regulations (IRR) of Republic Act 9184 (RA 9184), otherwise known as the “Government Procurement Reform Act.”

Bidding is restricted to Filipino citizens/sole proprietorships, cooperatives, and partnerships or organizations with at least seventy five percent (75%) interest or outstanding capital stock belonging to citizens of the Philippines.

- Interested bidders may obtain further information from Engineering Services Division, Philippine Ports Authority, PMO-Panay/Guimaras and inspect the Bidding Documents at the address given below from 8:00am to 5:00pm.

- A complete set of Bidding Documents may be acquired by interested bidders starting                August 9, 2017 from the address below and upon payment of the applicable fee for the Bidding Documents, pursuant to the latest Guidelines issued by the GPPB, in the amount of Ten Thousand Pesos only (P10, 000.00) VAT Exclusive.

It may also be downloaded free of charge from the website of the Philippine Government Electronic Procurement System (PhilGEPS) and the website of the Procuring Entity, provided that bidders shall pay the applicable fee for the Bidding Documents not later than the submission of their bids.

- The Philippine Ports Authority, PMO-Panay/Guimaras will hold a Pre-Bid Conference on August 16, 2017, 10:00 A.M at the PPA Conference Room, 2rd Floor, Admin. Bldg., ICPC, Iloilo City which shall be open to prospective bidders.

- Bids must be duly received by the BAC Secretariat at the address below on or before August 29, 2017 at 8:30 in the morning at the PPA Conference Room, 2rd Floor, Admin. Bldg., ICPC, Iloilo City.  All bids must be accompanied by a bid security in any of the acceptable forms and in the amount stated in ITB Clause 18.

Bid opening shall be on August 29, 2017 at 9:00 in the morning at the PPA Conference Room, 2rd Floor, Admin. Bldg., ICPC, Iloilo City. Bids will be opened in the presence of the bidders’ representatives who choose to attend at the address below. Late bids shall not be accepted.

- Other necessary information:

Required Equipments:

- Grinder/Tile Cutter

- Stake Truck 1 - Electric Cutter 1 - Oxy-cutting outfit

- Required PCAB License: General Building  – Small B

- The Philippine Ports Authority, PMO-Panay/Guimaras reserves the right to reject any and all bids, declare a failure of bidding, or not award the contract at any time prior to contract award in accordance with Section 41 of RA 9184 and its IRR, without thereby incurring any liability to the affected bidder or bidders.

- For further information, please refer to:

Engr. Rona Mae B. Barabona

BAC Secretariat

Philippine Ports Authority, PMO-Panay/Guimaras

Brgy. Loboc, Lapaz, Iloilo City

(033) 337-7791 local 302-302

esd_pmoiloilo@yahoo.com

ANTONIO F. BELARGA

Chairperson, BAC-EP

# Section II. Instructions to Bidders

Notes on the Instructions to Bidders This Section of the Bidding Documents provides the information necessary for Bidders to prepare responsive bids, in accordance with the requirements of the Procuring Entity. It also provides information on the bid submission, eligibility check, opening and evaluation of bids, and on the award of contract. This Section also contains provisions that are to be used unchanged. Section III. Bid Data Sheet consists of provisions that supplement, amend, or specify in detail information or requirements included in this Section and which are specific to each procurement. Matters governing the performance of the Contractor, payments under the contract, or matters affecting the risks, rights, and obligations of the parties under the contract are not normally included in this Section, but rather under Section IV. General Conditions of Contract (GCC), and/or Section V. Special Conditions of Contract (SCC). If duplication of a subject is inevitable in the other sections of the document prepared by the Procuring Entity, care must be exercised to avoid contradictions between clauses dealing with the same matter.

TABLE OF CONTENTS

A.	General	13

1.	Scope of Bid	13

2.	Source of Funds	13

3.	Corrupt, Fraudulent, Collusive, Coercive, and Obstructive Practices	13

4.	Conflict of Interest	15

5.	Eligible Bidders	16

6.	Bidder’s Responsibilities	17

7.	Origin of GOODS and Services	20

8.	Subcontracts	20

B.	Contents of Bidding Documents	20

9.	Pre-Bid Conference	20

10.	Clarification and Amendment of Bidding Documents	21

C.	Preparation of Bids	21

11.	Language of Bids	21

12.	Documents Comprising the Bid: Eligibility and Technical Components	22

13.	Documents Comprising the Bid: Financial Component	24

14.	Alternative Bids	25

15.	Bid Prices	25

16.	Bid Currencies	26

17.	Bid Validity	26

18.	Bid Security	26

19.	Format and Signing of Bids	29

20.	Sealing and Marking of Bids	29

D.	Submission and Opening of Bids	30

21.	Deadline for Submission of Bids	30

22.	Late Bids	30

23.	Modification and Withdrawal of Bids	30

24.	Opening and Preliminary Examination of Bids	31

E.	Evaluation and Comparison of Bids	33

25.	Process to be Confidential	33

26.	Clarification of Bids	33

27.	Detailed Evaluation and Comparison of Bids	33

28.	Post Qualification	34

29.	Reservation Clause	35

F.	Award of Contract	36

30.	Contract Award	36

31.	Signing of the Contract	37

32.	Performance Security	38

33.	Notice to Proceed	39

34. 	Protest Mechanism………………………………………………………………..36

## General

### Scope of Bid

The Procuring Entity named in the BDS, invites bids for the construction of Works, as described in Section VI. Specifications.

The name, identification, and number of lots specific to this bidding are provided in the BDS. The contracting strategy and basis of evaluation of lots is described in ITB Clause 27.

The successful Bidder will be expected to complete the Works by the intended completion date specified in SCC Clause 1.17.

### Source of Funds

## The Procuring Entity has a budget or received funds from the Funding Source named in the BDS, and in the amount indicated in the BDS.  It intends to apply part of the funds received for the Project, as defined in the BDS, to cover eligible payments under the Contract for the Works.

### Corrupt, Fraudulent, Collusive, Coercive, and Obstructive Practices

Unless otherwise specified in the BDS, the Procuring Entity, as well as bidders and contractors, shall observe the highest standard of ethics during the procurement and execution of the contract.  In pursuance of this policy, the Funding Source:

      - defines, for purposes of this provision, the terms set forth below as follows:

        - "corrupt practice" means behavior on the part of officials in the public or private sectors by which they improperly and unlawfully enrich themselves, others, or induce others to do so, by misusing the position in which they are placed, and includes the offering, giving, receiving, or soliciting of anything of value to influence the action of any such official in the procurement process or in contract execution; entering, on behalf of the Procuring Entity, into any contract or transaction manifestly and grossly disadvantageous to the same, whether or not the public officer profited or will profit thereby, and similar acts as provided in Republic Act 3019;

        - "fraudulent practice" means a misrepresentation of facts in order to influence a procurement process or the execution of a contract to the detriment of the Procuring Entity, and includes collusive practices among Bidders (prior to or after Bid submission) designed to establish bid prices at artificial, non-competitive levels and to deprive the Procuring Entity of the benefits of free and open competition;

        - “collusive practices” means a scheme or arrangement between two or more Bidders, with or without the knowledge of the Procuring Entity, designed to establish bid prices at artificial, non-competitive levels; and

        - “coercive practices” means harming or threatening to harm, directly or indirectly, persons, or their property to influence their participation in a procurement process, or affect the execution of  a contract;

        - “obstructive practice” is

(aa) 	deliberately destroying, falsifying, altering or concealing of evidence material to an administrative proceedings or investigation or making false statements to investigators in order to materially impede an administrative proceedings or investigation of the Procuring Entity or any foreign government/foreign or international financing institution into allegations of a corrupt, fraudulent, coercive or collusive practice; and/or threatening, harassing or intimidating any party to prevent it from disclosing its knowledge of matters relevant to the administrative proceedings or investigation or from pursuing such proceedings or investigation; or

(bb) 	acts intended to materially impede the exercise of the inspection and audit rights of the Procuring Entity or any foreign government/foreign or international financing institution herein.

      - will reject a proposal for award if it determines that the Bidder recommended for award has engaged in corrupt or fraudulent practices in competing for the Contract; and

      - will declare a firm ineligible, either indefinitely or for a stated period of time, to be awarded Contract funded by the Funding Source if it at any time determines that the firm has engaged in corrupt or fraudulent practices in competing or, or in executing, a Contract funded by the Funding Source.

Further, the Procuring Entity will seek to impose the maximum civil, administrative, and/or criminal penalties available under the applicable laws on individuals and organizations deemed to be involved in any of the practices mentioned in ITB Clause 3.1(a).

Furthermore, the Funding Source and the Procuring Entity reserve the right to inspect and audit records and accounts of a contractor in the bidding for and performance of a contract themselves or through independent auditors as reflected in the GCC Clause 34.

### Conflict of Interest

## All Bidders found to have conflicting interests shall be disqualified to participate in the procurement at hand, without prejudice to the imposition of appropriate administrative, civil, and criminal sanctions. A Bidder may be considered to have conflicting interests with another Bidder in any of the events described in paragraphs (a) through (c) and a general conflict of interest in any of the circumstances set out in paragraphs (d) through (g) below:

      - A Bidder has controlling shareholders in common with another Bidder;

      - A Bidder receives or has received any direct or indirect subsidy from any other Bidder;

      - A Bidder has the same legal representative as that of another Bidder for purposes of this Bid;

      - A Bidder has a relationship, directly or through third parties, that puts them in a position to have access to information about or influence on the bid of another Bidder or influence the decisions of the Procuring Entity regarding this bidding process;

      - A Bidder submits more than one bid in this bidding process. However, this does not limit the participation of subcontractors in more than one bid;

      - A Bidder who participated as a consultant in the preparation of the design or technical specifications of the goods and related services that are the subject of the bid; or

      - A Bidder who lends, or temporarily seconds, its personnel to firms or organizations which are engaged in consulting services for the preparation related to procurement for or implementation of the project, if the personnel would be involved in any capacity on the same project.

In accordance with Section 47 of the IRR of RA 9184, all Bidding Documents shall be accompanied by a sworn affidavit of the Bidder that it is not related to the Head of the Procuring Entity (HoPE), members of the Bids and Awards Committee (BAC), members of the Technical Working Group (TWG), members of the BAC Secretariat, the head of the Project Management Office (PMO) or the end-user unit, and the project consultants, by consanguinity or affinity up to the third civil degree. On the part of the Bidder, this Clause shall apply to the following persons:

      - If the Bidder is an individual or a sole proprietorship, to the Bidder himself;

      - If the Bidder is a partnership, to all its officers and members;

      - If the Bidder is a corporation, to all its officers, directors, and controlling stockholders;

      - If the Bidder is a cooperative, to all its officers, directors, and controlling shareholders or members; and

      - If the Bidder is a joint venture (JV), the provisions of items (a), (b), (c) or (d) of this Clause shall correspondingly apply to each of the members of the said JV, as may be appropriate.

Relationship of the nature described above or failure to comply with this Clause will result in the automatic disqualification of a Bidder.

### Eligible Bidders

Unless otherwise indicated in the BDS, the following persons shall be eligible to participate in this Bidding:

      - Duly licensed Filipino citizens/sole proprietorships;

      - Partnerships duly organized under the laws of the Philippines and of which at least seventy five percent (75%) of the interest belongs to citizens of the Philippines;

      - Corporations duly organized under the laws of the Philippines, and of which at least seventy five percent (75%) of the outstanding capital stock belongs to citizens of the Philippines;

      - Cooperatives duly organized under the laws of the Philippines.

      - Persons/entities forming themselves into a JV, i.e., a group of two (2) or more persons/entities that intend to be jointly and severally responsible or liable for a particular contract: Provided, however, that, in accordance with Letter of Instructions No. 630, Filipino ownership or interest of the joint venture concerned shall be at least seventy five percent (75%): Provided, further, that joint ventures in which Filipino ownership or interest is less than seventy five percent (75%) may be eligible where the structures to be built require the application of techniques and/or technologies which are not adequately possessed by a person/entity meeting the seventy five percent (75%) Filipino ownership requirement: Provided, finally, that in the latter case, Filipino ownership or interest shall not be less than twenty five percent (25%). For this purpose, Filipino ownership or interest shall be based on the contributions of each of the members of the joint venture as specified in their JVA.

The Procuring Entity may also invite foreign bidders when provided for under any Treaty or International or Executive Agreement as specified in the BDS.

Government owned or controlled corporations (GOCCs) may be eligible to participate only if they can establish that they (a) are legally and financially autonomous, (b) operate under commercial law, and (c) are not attached agencies of the Procuring Entity.

(a)  The Bidder must have an experience of having completed a Single Largest Completed Contract (SLCC) that is similar to this Project, equivalent to at least fifty percent (50%) of the ABC adjusted, if necessary, by the Bidder to current prices using the Philippine Statistics Authority (PSA) consumer price index.  However, contractors under Small A and Small B categories without similar experience on the contract to be bid may be allowed to bid if the cost of such contract is not more than the Allowable Range of Contract Cost (ARCC) of their registration based on the guidelines as prescribed by the PCAB.

(b)  For Foreign-funded Procurement, the Procuring Entity and the foreign government/foreign or international financing institution may agree on another track record requirement, as specified in the BDS.

For this purpose, contracts similar to the Project shall be those described in the BDS.

The Bidder must submit a computation of its Net Financial Contracting Capacity (NFCC), which must be at least equal to the ABC to be bid, calculated as follows:

NFCC = [(Current assets minus current liabilities) (15)] minus the value of all outstanding or uncompleted portions of the projects under ongoing contracts, including awarded contracts yet to be started coinciding with the contract for this Project.

The values of the domestic bidder’s current assets and current liabilities shall be based on the latest Audited Financial Statements (AFS) submitted to the BIR.

For purposes of computing the foreign bidders’ NFCC, the value of the current assets and current liabilities shall be based on their audited financial statements prepared in accordance with international financial reporting standards.

### Bidder’s Responsibilities

The Bidder or its duly authorized representative shall submit a sworn statement in the form prescribed in Section IX. Bidding Forms as required in ITB Clause 12.1(b)(iii).

The Bidder is responsible for the following:

      - Having taken steps to carefully examine all of the Bidding   Documents;

      - Having acknowledged all conditions, local or otherwise, affecting the implementation of the contract;

      - Having made an estimate of the facilities available and needed for the contract to be bid, if any;

      - Having complied with its responsibility to inquire or secure Supplemental/Bid Bulletin/s as provided under ITB Clause 10.4.

      - Ensuring that it is not “blacklisted” or barred from bidding by the GoP or any of its agencies, offices, corporations, or LGUs, including foreign government/foreign or international financing institution whose blacklisting rules have been recognized by the GPPB;

      - Ensuring that each of the documents submitted in satisfaction of the bidding requirements is an authentic copy of the original, complete, and all statements and information provided 	therein are true and correct;

      - Authorizing the HoPE or its duly authorized representative/s to verify all the documents submitted;

      - Ensuring that the signatory is the duly authorized representative of the Bidder, and granted full power and authority to do, execute and perform any and all acts necessary to participate, submit the bid, and to sign and execute the ensuing contract, accompanied by the duly notarized Special Power of Attorney, Board/Partnership Resolution, or Secretary’s Certificate, whichever is applicable;

      - Complying with the disclosure provision under Section 47 of RA 9184 and its IRR in relation to other provisions of RA 3019;

      - Complying with existing labor laws and standards, in the case of procurement of services. Moreover, bidder undertakes to:

        - Ensure the entitlement of workers to wages, hours of work, safety and health and other prevailing conditions of work as established by national laws, rules and regulations; or collective bargaining agreement; or arbitration award, if and when applicable.

In case there is a finding by the Procuring Entity or the DOLE of underpayment or non-payment of workers’ wage and wage-related benefits, bidder agrees that the performance security or portion of the contract amount shall be withheld in favor of the complaining workers pursuant to appropriate provisions of Republic Act No. 9184 without prejudice to the institution of appropriate actions under the Labor Code, as amended, and other social legislations.

        - Comply with occupational safety and health standards and to correct deficiencies, if any.

In case of imminent danger, injury or death of the worker, bidder undertakes to suspend contract implementation pending clearance to proceed from the DOLE Regional Office and to comply with Work Stoppage Order; and

        - Inform the workers of their conditions of work, labor clauses under the contract specifying wages, hours of work and other benefits under prevailing national laws, rules and regulations; or collective bargaining agreement; or arbitration award, if and when applicable, through posting in two (2) conspicuous places in the establishment’s premises; and

      - Ensuring that it did not give or pay, directly or indirectly, any commission, amount, fee, or any form of consideration, pecuniary or otherwise, to any person or official, personnel or representative of the;

Failure to observe any of the above responsibilities shall be at the risk of the Bidder concerned.

The Bidder, by the act of submitting its bid, shall be deemed to have inspected the site, determined the general characteristics of the contract works and the conditions for this Project and examine all instructions, forms, terms, and project requirements in the Bidding Documents.

It shall be the sole responsibility of the prospective bidder to determine and to satisfy itself by such means as it considers necessary or desirable as to all matters pertaining to this Project, including: (a) the location and the nature of the contract, project, or work; (b) climatic conditions; (c) transportation facilities; (c) nature and condition of the terrain, geological conditions at the site communication facilities, requirements, location and availability of construction aggregates and other materials, labor, water, electric power and access roads; and (d) other factors that may affect the cost, duration and execution or implementation of the contract, project, or work.

The Procuring Entity shall not assume any responsibility regarding erroneous interpretations or conclusions by the prospective or eligible bidder out of the data furnished by the procuring entity.  However, the Procuring Entity shall ensure that all information in the Bidding Documents, including supplemental/bid bulletins issued are correct and consistent.

Before submitting their bids, the Bidders are deemed to have become familiar with all existing laws, decrees, ordinances, acts and regulations of the Philippines which may affect the contract in any way.

The Bidder shall bear all costs associated with the preparation and submission of his bid, and the Procuring Entity will in no case be responsible or liable for those costs, regardless of the conduct or outcome of the bidding process.

The Bidder should note that the Procuring Entity will accept bids only from those that have paid the applicable fee for the Bidding Documents at the office indicated in the Invitation to Bid.

### Origin of Goods and Services

## There is no restriction on the origin of Goods, or Contracting of Works or Services other than those prohibited by a decision of the United Nations Security Council taken under Chapter VII of the Charter of the United Nations.

### Subcontracts

Unless otherwise specified in the BDS, the Bidder may subcontract portions of the Works to an extent as may be approved by the Procuring Entity and stated in the BDS. However, subcontracting of any portion shall not relieve the Bidder from any liability or obligation that may arise from the contract for this Project.

Subcontractors must submit the documentary requirements under ITB Clause 12 and comply with the eligibility criteria specified in the BDS. In the event that any subcontractor is found by the Procuring Entity to be ineligible, the subcontracting of such portion of the Works shall be disallowed.

The Bidder may identify the subcontractor to whom a portion of the Works will be subcontracted at any stage of the bidding process or during contract implementation.   If the Bidder opts to disclose the name of the subcontractor during bid submission, the Bidder shall include the required documents as part of the technical component of its bid.

## Contents of Bidding Documents

### Pre-Bid Conference

(a)  If so specified in the BDS, a pre-bid conference shall be held at the venue and on the date indicated therein, to clarify and address the Bidders’ questions on the technical and financial components of this Project.

(b) The pre-bid conference shall be held at least twelve (12) calendar days before the deadline for the submission of and receipt of bids, but not earlier than seven (7) calendar days from the posting of the Invitation to Bid/Bidding Documents in the PhilGEPS website. If the Procuring Entity determines that, by reason of the method, nature, or complexity of the contract to be bid, or when international participation will be more advantageous to the GoP, a longer period for the preparation of bids is necessary, the pre-bid conference shall be held at least thirty (30) calendar days before the deadline for the submission and receipt of bids, as specified in the BDS.

Bidders are encouraged to attend the pre-bid conference to 	ensure that they fully understand the Procuring Entity’s requirements.  Non-attendance of the Bidder will in no way prejudice its bid; however, the Bidder is expected to know the changes and/or amendments to the Bidding Documents as recorded in the minutes of the pre-bid conference and the Supplemental/Bid Bulletin. The minutes of the pre-bid conference shall be recorded and prepared not later than five (5) calendar days after the pre-bid conference. The minutes shall be made available to prospective bidders not later than five (5) days upon written request.

Decisions of the BAC amending any provision of the bidding documents shall be issued in writing through a Supplemental/Bid Bulletin at least seven (7) calendar days before the deadline for the submission and receipt of bids.

### Clarification and Amendment of Bidding Documents

Prospective bidders may request for clarification(s) on and/or interpretation of any part of the Bidding Documents. Such a request must be in writing and submitted to the Procuring Entity at the address indicated in the BDS at least ten (10) calendar days before the deadline set for the submission and receipt of Bids.

The BAC shall respond to the said request by issuing a Supplemental/Bid Bulletin, to be made available to all those who have properly secured the Bidding Documents, at least seven (7) calendar days before the deadline for the submission and receipt of Bids.

Supplemental/Bid Bulletins may also be issued upon the Procuring Entity’s initiative for purposes of clarifying or modifying any provision of the Bidding Documents not later than seven (7) calendar days before the deadline for the submission and receipt of Bids.  Any modification to the Bidding Documents shall be identified as an amendment.

Any Supplemental/Bid Bulletin issued by the BAC shall also be posted in the PhilGEPS and the website of the Procuring Entity concerned, if available, and at any conspicuous place in the premises of the Procuring Entity concerned. It shall be the responsibility of all Bidders who have properly secured the Bidding Documents to inquire and secure Supplemental/Bid Bulletins that may be issued by the BAC. However, Bidders who have submitted bids before the issuance of the Supplemental/Bid Bulletin must be informed and allowed to modify or withdraw their bids in accordance with ITB Clause 23.

## Preparation of Bids

### Language of Bids

The eligibility requirements or statements, the bids, and all other documents to be submitted to the BAC must be in English. If the eligibility requirements or statements, the bids, and all other documents submitted to the BAC are in foreign language other than English, it must be accompanied by a translation of the documents in English. The documents shall be translated by the relevant foreign government agency, the foreign government agency authorized to translate documents, or a registered translator in the foreign bidder’s country; and shall be authenticated by the appropriate Philippine foreign service establishment/post or the equivalent office having jurisdiction over the foreign bidder’s affairs in the Philippines. The English translation shall govern, for purposes of interpretation of the bid.

### Documents Comprising the Bid: Eligibility and Technical Components

Unless otherwise indicated in the BDS, the first envelope shall contain the following eligibility and technical documents:

      - Eligibility Documents –

Class “A” Documents

              - PhilGEPS Certificate of Registration and Membership in accordance with Section 8.5.2 of the IRR, except for foreign bidders participating in the procurement by a Philippine Foreign Service Office or Post, which shall submit their eligibility documents under Section 23.1 of the IRR, provided, that the winning bidder shall register with the PhilGEPS in accordance with Section 37.1.4 of the IRR;

              - Statement of all its ongoing government and private contracts, including contracts awarded but not yet started, if any, whether similar or not similar in nature and complexity to the contract to be bid; and

Statement of the Bidder’s SLCC similar to the contract to be bid, in accordance with ITB Clause 5.4.

The two statements required shall indicate for each contract the following:

(ii.1) 	name of the contract;

(ii.2) 	date of the contract;

(ii.3) 	contract duration;

(ii.4)	owner’s name and address;

(ii.5)	nature of work;

(ii.6) 	contractor’s role (whether sole contractor, subcontractor, or partner in a JV) and percentage of participation;

(ii.7) 	total contract value at award;

(ii.8) 	date of completion or estimated completion time;

(ii.9) 	total contract value at completion, if applicable;

(ii.10) 	percentages of planned and actual accomplishments, if applicable; and

(ii.11) 	value of outstanding works, if applicable.

The statement of the Bidder’s SLCC shall be supported by the Notice of Award and/or Notice to Proceed, Project Owner’s Certificate of Final Acceptance issued by the Owner other than the Contractor or the Constructors Performance Evaluation System (CPES) Final Rating, which must be at least satisfactory. In case of contracts with the private sector, an equivalent document shall be submitted;

              - Unless otherwise provided in the BDS, a valid special PCAB License in case of joint ventures, and registration for the type and cost of the contract for this Project; and

              - NFCC computation in accordance with ITB Clause 5.5.

Class “B” Documents

              - If applicable, Joint Venture Agreement (JVA) in accordance with RA 4566.

      - Technical Documents –

        - Bid security in accordance with ITB Clause 18. If the Bidder opts to submit the bid security in the form of:

          - a bank draft/guarantee or an irrevocable letter of credit issued by a foreign bank, it shall be accompanied by a confirmation from a Universal or Commercial Bank; or

          - a surety bond accompanied by a certification coming from the Insurance Commission that the surety or insurance company is authorized to issue such instruments.

        - Project Requirements, which shall include the following:

          - Organizational chart for the contract to be bid;

          - List of contractor’s personnel (e.g., Project Manager, Project Engineers, Materials Engineers, and Foremen), to be assigned to the contract to be bid, with their complete qualification and experience data. These personnel must meet the required minimum years of experience set in the BDS; and

          - List of contractor’s major equipment units, which are owned, leased, and/or under purchase agreements, supported by proof of ownership, certification of availability of equipment from the equipment lessor/vendor for the duration of the project, as the case may be, which must meet the minimum requirements for the contract set in the BDS; and

        - Sworn statement in accordance with Section 25.3 of the IRR of RA 9184 and using the form prescribed in Section IX. Bidding Forms.

### Documents Comprising the Bid: Financial Component

Unless otherwise stated in the BDS, the financial component of the bid shall contain the following:

      - Financial Bid Form, which includes bid prices and the bill of quantities, in accordance with ITB Clauses 15.1 and 15.3; and

      - Any other document related to the financial component of the bid as stated in the BDS.

(a)	Unless otherwise stated in the BDS, all Bids that exceed the ABC shall not be accepted.

(b)	Unless otherwise indicated in the BDS, for foreign-funded procurement, a ceiling may be applied to bid prices provided the following conditions are met:

(i)   Bidding Documents are obtainable free of charge on a freely accessible website.  If payment of Bidding Documents is required by the procuring entity, payment could be made upon the submission of bids.

(ii)   The procuring entity has procedures in place to ensure that the ABC is based on recent estimates made by the engineer or the responsible unit of the procuring entity and that the estimates are based on adequate detailed engineering (in the case of infrastructure projects) and reflect the quality, supervision and risk and inflationary factors, as well as prevailing market prices, associated with the types of works or goods to be procured.

(iii)  The procuring entity has trained cost estimators on estimating prices and analyzing bid variances. In the case of infrastructure projects, the procuring entity must also have trained quantity surveyors.

(iv)  The procuring entity has established a system to monitor and report bid prices relative to ABC and engineer’s/procuring entity’s estimate.

(v)  The procuring entity has established a monitoring and evaluation system for contract implementation to provide a feedback on actual total costs of goods and works.

### Alternative Bids

Alternative Bids shall be rejected. For this purpose, alternative bid is an offer made by a Bidder in addition or as a substitute to its original bid which may be included as part of its original bid or submitted separately therewith for purposes of bidding. A bid with options is considered an alternative bid regardless of whether said bid proposal is contained in a single envelope or submitted in two (2) or more separate bid envelopes.

Bidders shall submit offers that comply with the requirements of the Bidding Documents, including the basic technical design as indicated in the drawings and specifications.  Unless there is a value engineering clause in the BDS, alternative bids shall not be accepted.

Each Bidder shall submit only one Bid, either individually or as a partner in a JV.  A Bidder who submits or participates in more than one bid (other than as a subcontractor if a subcontractor is permitted to participate in more than one bid) will cause all the proposals with the Bidder’s participation to be disqualified. This shall be without prejudice to any applicable criminal, civil and administrative penalties that may be imposed upon the persons and entities concerned.

### Bid Prices

The contract shall be for the whole Works, as described in ITB Clause 1.1, based on the priced Bill of Quantities submitted by the Bidder.

The Bidder shall fill in rates and prices for all items of the Works described in the Bill of Quantities.  Bids not addressing or providing all of the required items in the Bidding Documents including, where applicable, Bill of Quantities, shall be considered non-responsive and, thus, automatically disqualified. In this regard, where a required item is provided, but no price is indicated, the same shall be considered as non-responsive, but specifying a zero (0) or a  dash (-) for the said item would mean that it is being offered for free to the Government, except those required by law or regulations to be provided for.

All duties, taxes, and other levies payable by the Contractor under the Contract, or for any other cause, prior to the deadline for submission of bids, shall be included in the rates, prices, and total bid price submitted by the Bidder.

All bid prices for the given scope of work in the contract as awarded shall be considered as fixed prices, and therefore not subject to price escalation during contract implementation, except under extraordinary circumstances as specified in GCC Clause 48. Upon the recommendation of the Procuring Entity, price escalation may be allowed in extraordinary circumstances as may be determined by the National Economic and Development Authority in accordance with the Civil Code of the Philippines, and upon approval by the GPPB. Furthermore, in cases where the cost of the awarded contract is affected by any applicable new laws, ordinances, regulations, or other acts of the GoP, promulgated after the date of bid opening, a contract price adjustment shall be made or appropriate relief shall be applied on a no loss-no gain basis.

### Bid Currencies

All bid prices shall be quoted in Philippine Pesos unless otherwise provided in the BDS. However, for purposes of bid evaluation, bids denominated in foreign currencies shall be converted to Philippine currency based on the exchange rate prevailing on the day of the Bid Opening.

If so allowed in accordance with ITB Clause 16.1, the Procuring Entity for purposes of bid evaluation and comparing the bid prices will convert the amounts in various currencies in which the bid price is expressed to Philippine Pesos at the exchange rate as published in the Bangko Sentral ng Pilipinas (BSP) reference rate bulletin on the day of the bid opening.

Unless otherwise specified in the BDS, payment of the contract price shall be made in Philippine Pesos.

### Bid Validity

Bids shall remain valid for the period specified in the BDS which shall not exceed one hundred twenty (120) calendar days from the date of the opening of bids.

In exceptional circumstances, prior to the expiration of the bid validity period, the Procuring Entity may request Bidders to extend the period of validity of their bids. The request and the responses shall be made in writing. The bid security described in ITB Clause 18 should also be extended corresponding to the extension of the bid validity period at the least. A Bidder may refuse the request without forfeiting its bid security, but his bid shall no longer be considered for further evaluation and award. A Bidder granting the request shall not be required or permitted to modify its bid.

### Bid Security

The Bidder shall submit a Bid Securing Declaration or any form of Bid Security in an amount stated in the BDS, which shall be not less than the percentage of the ABC in accordance with the following schedule:

| Form of Bid Security | Amount of Bid Security (Not less than the Percentage of the ABC) |
| --- | --- |
| Cash or cashier’s/manager’s check issued by a Universal or Commercial Bank. For biddings conducted by LGUs, the cashier’s/manager’s check may be issued by other banks certified by the BSP as authorized to issue such financial instrument. | Two percent (2%) |
| Bank draft/guarantee or irrevocable letter of credit issued by a Universal or Commercial Bank: Provided, however, that it shall be confirmed or authenticated by a Universal or Commercial Bank, if issued by a foreign bank. For biddings conducted by LGUs, the Bank Draft/ Guarantee, or irrevocable letter of credit may be issued by other banks certified by the BSP as authorized to issue such financial instrument. |  |
| Surety bond callable upon demand issued by a surety or insurance company duly certified by the Insurance Commission as authorized to issue such security; and/or | Five percent (5%) |

The Bid Securing Declaration mentioned above is an undertaking which states, among others, that the Bidder shall enter into contract with the procuring entity and furnish the performance security required under ITB Clause 32.2, within ten (10) calendar days from receipt of the Notice of Award, and commits to pay the corresponding amount as fine, and be suspended for a period of time from being qualified to participate in any government procurement activity in the event it violates any of the conditions stated therein as provided in the guidelines issued by the GPPB.

The bid security should be valid for the period specified in the BDS.  Any bid not accompanied by an acceptable bid security shall be rejected by the Procuring Entity as non-responsive.

No bid securities shall be returned to Bidders after the opening of bids and before contract signing, except to those that failed or declared as post-disqualified, upon submission of a written waiver of their right to file a request for reconsideration and/or protest, or lapse of the reglementary period without having filed a request for reconsideration or protest.  Without prejudice on its forfeiture, Bid Securities shall be returned only after the Bidder with the Lowest Calculated Responsive Bid (LCRB) has signed the contract and furnished the Performance Security, but in no case later than the expiration of the Bid Security validity period indicated in ITB Clause 18.2.

Upon signing and execution of the contract, pursuant to ITB Clause 31, and the posting of the performance security, pursuant to ITB Clause 32, the successful Bidder’s Bid Security will be discharged, but in no case later than the Bid Security validity period as indicated in ITB Clause 18.2.

The bid security may be forfeited:

      - if a Bidder:

        - withdraws its bid during the period of bid validity specified in ITB Clause 17;

        - does not accept the correction of errors pursuant to ITB Clause 27.3(b);

        - has a finding against the veracity of the required documents submitted in accordance with ITB Clause 28.2;

        - submission of eligibility requirements containing false information or falsified documents;

        - submission of bids that contain false information or falsified documents, or the concealment of such information in the bids in order to influence the outcome of eligibility screening or any other stage of the public bidding;

        - allowing the use of one’s name, or using the name of another for purposes of public bidding;

        - withdrawal of a bid, or refusal to accept an award, or enter into contract with the Government without justifiable cause, after the Bidder had been adjudged as having submitted the LCRB;

        - refusal or failure to post the required performance security within the prescribed time;

        - refusal to clarify or validate in writing its bid during post-qualification within a period of seven (7) calendar days from receipt of the request for clarification;

        - any documented attempt by a Bidder to unduly influence the outcome of the bidding in his favor;

        - failure of the potential joint venture partners to enter into the joint venture after the bid is declared successful; or

        - all other acts that tend to defeat the purpose of the competitive bidding, such as habitually withdrawing from bidding, submitting late Bids or patently insufficient bid, for at least three (3) times within a year, except for valid reasons.

      - if the successful Bidder:

        - fails to sign the contract in accordance with ITB Clause 31;

        - fails to furnish performance security in accordance with ITB Clause 32.

### Format and Signing of Bids

  - Bidders shall submit their bids through their duly authorized representative using the appropriate forms provided in Section IX. Bidding Forms on or before the deadline specified in the ITB Clause 21 in two (2) separate sealed bid envelopes, and which shall be submitted simultaneously. The first shall contain the technical component of the bid, including the eligibility requirements under ITB Clause 12.1, and the second shall contain the financial component of the bid. This shall also be observed for each lot in the case of lot procurement.

19.2 	Forms as mentioned in ITB Clause 19.1 must be completed without any alterations to their format, and no substitute form shall be accepted. All blank spaces shall be filled in with the information requested.

19.3 	The Bidder shall prepare and submit an original of the first and second envelopes as described in ITB Clauses 12 and 13.  In addition, the Bidder shall submit copies of the first and second envelopes.  In the event of any discrepancy between the original and the copies, the original shall prevail.

19.4 	Each and every page of the Bid Form, including the Bill of Quantities, under Section IX hereof, shall be signed by the duly authorized representative/s of the Bidder. Failure to do so shall be a ground for the rejection of the bid.

  - Any interlineations, erasures, or overwriting shall be valid only if they are signed or initialed by the duly authorized representative/s of the Bidder.

### Sealing and Marking of Bids

Bidders shall enclose their original eligibility and technical documents described in ITB Clause 12, in one sealed envelope marked “ORIGINAL - TECHNICAL COMPONENT,” and the original of their financial component in another sealed envelope marked “ORIGINAL - FINANCIAL COMPONENT,” sealing them all in an outer envelope marked “ORIGINAL BID.”

Each copy of the first and second envelopes shall be similarly sealed duly marking the inner envelopes as “COPY NO. ___ - TECHNICAL COMPONENT” and “COPY NO. ___ – FINANCIAL COMPONENT” and the outer envelope as “COPY NO. ___,” respectively.  These envelopes containing the original and the copies shall then be enclosed in one single envelope.

The original and the number of copies of the bid as indicated in the BDS shall be typed or written in ink and shall be signed by the Bidder or its duly authorized representative/s.

All envelopes shall:

      - contain the name of the contract to be bid in capital letters;

      - bear the name and address of the Bidder in capital letters;

      - be addressed to the Procuring Entity’s BAC in accordance with ITB Clause 20.1;

      - bear the specific identification of this bidding process indicated in the ITB Clause 1.2; and

      - bear a warning “DO NOT OPEN BEFORE…” the date and time for the opening of bids, in accordance with ITB Clause 21.

Bid envelopes that are not properly sealed and marked, as required in the bidding documents, shall not be rejected, but the Bidder or its duly authorized representative shall acknowledge such condition of the bid as submitted. The BAC or the Procuring Entity shall assume no responsibility for the misplacement of the contents of the improperly sealed or marked bid, or for its premature opening.

## Submission and Opening of Bids

### Deadline for Submission of Bids

Bids must be received by the Procuring Entity’s BAC at the address and on or before the date and time indicated in the BDS.

### Late Bids

Any bid submitted after the deadline for submission and receipt of bids prescribed by the Procuring Entity, pursuant to ITB Clause 21, shall be declared “Late” and shall not be accepted by the Procuring Entity. The BAC shall record in the minutes of Bid Submission and Opening, the Bidder’s name, its representative and the time the late bid was submitted.

### Modification and Withdrawal of Bids

The Bidder may modify its bid after it has been submitted; provided that the modification is received by the Procuring Entity prior to the deadline prescribed for submission and receipt of bids. The Bidder shall not be allowed to retrieve its original bid, but shall be allowed to submit another bid equally sealed and properly identified in accordance with Clause 20, linked to its original bid marked as “TECHNICAL MODIFICATION” or “FINANCIAL MODIFICATION” and stamped “received” by the BAC. Bid modifications received after the applicable deadline shall not be considered and shall be returned to the Bidder unopened.

A Bidder may, through a Letter of Withdrawal, withdraw its bid after it has been submitted, for valid and justifiable reason; provided that the Letter of Withdrawal is received by the Procuring Entity prior to the deadline prescribed for submission and receipt of bids. The Letter of Withdrawal must be executed by the authorized representative of the Bidder identified in the Omnibus Sworn Statement, a copy of which should be attached to the letter.

Bids requested to be withdrawn in accordance with ITB Clause 23.1 shall be returned unopened to the Bidders. A Bidder, who has acquired the bidding documents may also express its intention not to participate in the bidding through a letter which should reach and be stamped by the BAC before the deadline for submission and receipt of bids. A Bidder that withdraws its bid shall not be permitted to submit another bid, directly or indirectly, for the same contract.

No bid may be modified after the deadline for submission of bids. No bid may be withdrawn in the interval between the deadline for submission of bids and the expiration of the period of bid validity specified by the Bidder on the Financial Bid Form.  Withdrawal of a bid during this interval shall result in the forfeiture of the Bidder’s bid security, pursuant to ITB Clause 18.5, and the imposition of administrative, civil, and criminal sanctions as prescribed by RA 9184 and its IRR.

### Opening and Preliminary Examination of Bids

The BAC shall open the Bids in public, immediately after the deadline for the submission and receipt of bids in public, as specified in the BDS. In case the Bids cannot be opened as scheduled due to justifiable reasons, the BAC shall take custody of the Bids submitted and reschedule the opening of Bids on the next working day or at the soonest possible time through the issuance of a Notice of Postponement to be posted in the PhilGEPS website and the website of the Procuring Entity concerned.

Unless otherwise specified in the BDS, the BAC shall open the first bid envelopes and determine each Bidder’s compliance with the documents prescribed in ITB Clause 12, using a non-discretionary “pass/fail” criterion. If a Bidder submits the required document, it shall be rated “passed” for that particular requirement. In this regard, bids that fail to include any requirement or are incomplete or patently insufficient shall be considered as “failed”. Otherwise, the BAC shall rate the said first bid envelope as “passed”.

Unless otherwise specified in the BDS, immediately after determining compliance with the requirements in the first envelope, the BAC shall forthwith open the second bid envelope of each remaining eligible Bidder whose first bid envelope was rated “passed.” The second envelope of each complying Bidder shall be opened within the same day. In case one or more of the requirements in the second envelope of a particular bid is missing, incomplete or patently insufficient, and/or if the submitted total bid price exceeds the ABC unless otherwise provided in ITB Clause 13.2, the BAC shall rate the bid concerned as “failed.” Only bids that are determined to contain all the bid requirements for both components shall be rated “passed” and shall immediately be considered for evaluation and comparison.

Letters of Withdrawal shall be read out and recorded during bid opening, and the envelope containing the corresponding withdrawn bid shall be returned to the Bidder unopened.

All members of the BAC who are present during bid opening shall initial every page of the original copies of all bids received and opened.

In the case of an eligible foreign bidder as described in ITB Clause 5, the following Class “A” Documents may be substituted with the appropriate equivalent documents, if any, issued by the country of the foreign bidder concerned, which shall likewise be uploaded and maintained in the PhilGEPS in accordance with Section 8.5.2 of the IRR.:

- Registration certificate from the Securities and Exchange Commission (SEC), Department of Trade and Industry (DTI) for sole proprietorship, or CDA for cooperatives;

- Mayor’s/Business permit issued by the local government where the principal place of business of the Bidder is located; and

- Audited Financial Statements showing, among others, the prospective Bidder’s total and current assets and liabilities stamped “received” by the Bureau of Internal Revenue or its duly accredited and authorized institutions, for the preceding calendar year which should not be earlier than two years from the date of bid submission.

Each partner of a joint venture agreement shall likewise submit the document required in ITB Clause 12.1(a)(i). Submission of documents required under ITB Clauses 12.1(a)(ii) to 12.1(a)(iv) by any of the joint venture partners constitutes compliance.

The Procuring Entity shall prepare the minutes of the proceedings of the bid opening that shall include,  as a minimum: (a) names of Bidders, their bid price (per lot, if applicable, and/or including discount, if any), bid security, findings of preliminary examination, and whether there is a withdrawal or modification; and (b) attendance sheet. The BAC members shall sign the abstract of bids as read.

24.8. 	The Bidders or their duly authorized representatives may attend the opening of bids. The BAC shall ensure the integrity, security, and confidentiality of all submitted bids. The Abstract of Bids as read and the minutes of the Bid Opening shall be made available to the public upon written request and payment of a specified fee to recover cost of materials.

24.9	To ensure transparency and accurate representation of the bid submission, the BAC Secretariat shall notify in writing all Bidders whose bids it has received through its PhilGEPS-registered physical address or official e-mail address. The notice shall be issued within seven (7) calendar days from the date of the bid opening.

## Evaluation and Comparison of Bids

### Process to be Confidential

Members of the BAC, including its staff and personnel, as well as its Secretariat and TWG, are prohibited from making or accepting any kind of communication with any Bidder regarding the evaluation of their bids until the issuance of the Notice of Award, unless otherwise allowed in the case of ITB Clause 26.

Any effort by a Bidder to influence the Procuring Entity in the Procuring Entity’s decision in respect of bid evaluation, bid comparison or contract award will result in the rejection of the Bidder’s bid.

### Clarification of Bids

To assist in the evaluation, comparison and post-qualification of the bids, the Procuring Entity may ask in writing any Bidder for a clarification of its bid.  All responses to requests for clarification shall be in writing. Any clarification submitted by a Bidder in respect to its bid and that is not in response to a request by the Procuring Entity shall not be considered

### Detailed Evaluation and Comparison of Bids

The Procuring Entity will undertake the detailed evaluation and comparison of Bids which have passed the opening and preliminary examination of Bids, pursuant to ITB Clause 24, in order to determine the Lowest Calculated Bid.

The Lowest Calculated Bid shall be determined in two steps:

      - The detailed evaluation of the financial component of the bids, to establish the correct calculated prices of the bids; and

      - The ranking of the total bid prices as so calculated from the lowest to highest. The bid with the lowest price shall be identified as the Lowest Calculated Bid.

The Procuring Entity's BAC shall immediately conduct a detailed evaluation of all bids rated “passed,” using non-discretionary “pass/fail” criterion. The BAC shall consider the following in the evaluation of bids:

      - Completeness of the bid. Unless the BDS allows partial bids, bids  not addressing or providing all of the required items in the Schedule of Requirements including, where applicable, bill of quantities, shall be considered non-responsive and, thus, automatically disqualified. In this regard, where a required item is provided, but no price is indicated, the same shall be considered as non-responsive, but specifying a zero (0) or a dash (-) for the said item would mean that it is being offered for free to the Procuring Entity, except those required by law or regulations to be provided for; and

      - Arithmetical corrections. Consider computational errors and omissions to enable proper comparison of all eligible bids.  It may also consider bid modifications. Any adjustment shall be calculated in monetary terms to determine the calculated prices.

Based on the detailed evaluation of bids, those that comply with the above-mentioned requirements shall be ranked in the ascending order of their total calculated bid prices, as evaluated and corrected for computational errors, discounts and other modifications, to identify the Lowest Calculated Bid.  Total calculated bid prices, as evaluated and corrected for computational errors, discounts and other modifications, which exceed the ABC shall not be considered, unless otherwise indicated in the BDS.

The Procuring Entity’s evaluation of bids shall be based on the bid price quoted in the Bid Form, which includes the Bill of Quantities.

Bids shall be evaluated on an equal footing to ensure fair competition.  For this purpose, all Bidders shall be required to include in their bids the cost of all taxes, such as, but not limited to, value added tax (VAT), income tax, local taxes, and other fiscal levies and duties which shall be itemized in the bid form and reflected in the detailed estimates.  Such bids, including said taxes, shall be the basis for bid evaluation and comparison.

If so indicated pursuant to ITB Clause 1.2. Bids are being invited for individual lots or for any combination thereof, provided that all Bids and combinations of Bids shall be received by the same deadline and opened and evaluated simultaneously so as to determine the bid or combination of bids offering the lowest calculated cost to the Procuring Entity. Bid prices quoted shall correspond to all of the requirements specified for each lot. Bid Security as required by ITB Clause 18 shall be submitted for each contract (lot) separately. The basis for evaluation of lots is specified in BDS Clause 27.3.

### Post Qualification

The BAC shall determine to its satisfaction whether the Bidder that is evaluated as having submitted the Lowest Calculated Bid complies with and is responsive to all the requirements and conditions specified in ITB Clauses 5, 12, and 13.

Within a non-extendible period of five (5) calendar days from receipt by the Bidder of the notice from the BAC that it submitted the Lowest Calculated Bid, the Bidder shall submit its latest income and business tax returns filed and paid through the BIR Electronic Filing and Payment System (eFPS) and other appropriate licenses and permits required by law and stated in the BDS.

Failure to submit any of the post-qualification requirements on time, or a finding against the veracity thereof, shall disqualify the Bidder for award.  Provided in the event that a finding against the veracity of any of the documents submitted is made, it shall cause the forfeiture of the bid security in accordance with Section 69 of the IRR of RA 9184.

The determination shall be based upon an examination of the documentary evidence of the Bidder’s qualifications submitted pursuant to ITB Clauses 12 and 13, as well as other information as the Procuring Entity deems necessary and appropriate, using a non-discretionary “pass/fail” criterion, which shall be completed within a period of twelve (12) calendar days.

If the BAC determines that the Bidder with the Lowest Calculated Bid passes all the criteria for post-qualification, it shall declare the said bid as the LCRB, and recommend to the HoPE the award of contract to the said Bidder at its submitted price or its calculated bid price, whichever is lower, subject to ITB Clause 30.3.

A negative determination shall result in rejection of the Bidder’s bid, in which event the Procuring Entity shall proceed to the next Lowest Calculated Bid, with a fresh period to make a similar determination of that Bidder’s capabilities to perform satisfactorily. If the second Bidder, however, fails the post qualification, the procedure for post qualification shall be repeated for the Bidder with the next Lowest Calculated Bid, and so on until the LCRB is determined for recommendation of contract award.

Within a period not exceeding fifteen (15) calendar days from the determination by the BAC of the LCRB and the recommendation to award the contract, the HoPE or his duly authorized representative shall approve or disapprove the said recommendation.

In the event of disapproval, which shall be based on valid, reasonable, and justifiable grounds as provided for under Section 41 of the IRR of RA 9184, the HoPE shall notify the BAC and the Bidder in writing of such decision and the grounds for it. When applicable, the BAC shall conduct a post-qualification of the Bidder with the next Lowest Calculated Bid. A request for reconsideration may be filed by the Bidder with the HoPE in accordance with Section 37.1.3 of the IRR of RA 9184.

### Reservation Clause

Notwithstanding the eligibility or post-qualification of a Bidder, the Procuring Entity concerned reserves the right to review its qualifications at any stage of the procurement process if it has reasonable grounds to believe that a misrepresentation has been made by the said Bidder, or that there has been a change in the Bidder’s capability to undertake the project from the time it submitted its eligibility requirements.  Should such review uncover any misrepresentation made in the eligibility and bidding requirements, statements or documents, or any changes in the situation of the Bidder which will affect its capability to undertake the project so that it fails the preset eligibility or bid evaluation criteria, the Procuring Entity shall consider the said Bidder as ineligible and shall disqualify it from submitting a bid or from obtaining an award or contract.

Based on the following grounds, the Procuring Entity reserves the right to reject any and all Bids, declare a Failure of Bidding at any time prior to the contract award, or not to award the contract, without thereby incurring any liability, and make no assurance that a contract shall be entered into as a result of the bidding:

      - If there is prima facie evidence of collusion between appropriate public officers or employees of the Procuring Entity, or between the BAC and any of the Bidders, or if the collusion is between or among the Bidders themselves, or between a Bidder and a third party, including any act which restricts, suppresses or nullifies or tends to restrict, suppress or nullify competition;

      - If the Procuring Entity’s BAC is found to have failed in  following the prescribed bidding procedures; or

      - For any justifiable and reasonable ground where the award of the contract will not redound to the benefit of the GOP as follows:

        - If the physical and economic conditions have significantly changed so as to render the project no longer economically, financially or technically feasible as determined by the HoPE;

        - If the project is no longer necessary as determined by the HoPE; and

        - If the source of funds for the project has been withheld or reduced through no fault of the Procuring Entity.

In addition, the Procuring Entity may likewise declare a failure of bidding when:

      - No bids are received;

      - All prospective Bidders are declared ineligible;

      - All bids fail to comply with all the bid requirements, fail post-qualification; or

      - The Bidder with the LCRB refuses, without justifiable cause, to accept the award of contract, and no award is made in accordance with Section 40 of the IRR of RA 9184.

## Award of Contract

### Contract Award

Subject to ITB Clause 28, the HoPE or its duly authorized representative shall award the contract to the Bidder whose bid has been determined to be the LCRB.

Prior to the expiration of the period of bid validity, the Procuring Entity shall notify the successful Bidder in writing that its bid has been accepted, through a Notice of Award duly received by the Bidder or its representative personally or by registered mail or electronically, receipt of which must be confirmed in writing within two (2) days by the Bidder with the LCRB and submitted personally or sent by registered mail or electronically to the Procuring Entity.

Notwithstanding the issuance of the Notice of Award, award of contract shall be subject to the following conditions:

      - Submission of the following documents within ten (10) calendar days from receipt of the Notice of Award:

        - In the case of procurement by a Philippine Foreign Service Office or Post, the PhilGEPS Registration Number of the winning foreign Bidder; or

        - Valid PCAB license and registration for the type and cost of the contract to be bid for foreign bidders when the Treaty or International or Executive Agreement expressly allows submission of the PCAB license and registration for the type and cost of the contract to be bid as a pre-condition to the Award;

      - Posting of the performance security in accordance with ITB Clause 32;

      - Signing of the contract as provided in ITB Clause 31; and

      - Approval by higher authority, if required, as provided in Section 37.3 of the IRR of RA 9184.

### Signing of the Contract

At the same time as the Procuring Entity notifies the successful Bidder that its bid has been accepted, the Procuring Entity shall send the Contract Form to the Bidder, which Contract has been provided in the Bidding Documents, incorporating therein all agreements between the parties.

Within ten (10) calendar days from receipt of the Notice of Award, the successful Bidder shall post the required performance security, sign and date the contract and return it to the Procuring Entity.

The Procuring Entity shall enter into contract with the successful Bidder within the same ten (10) calendar day period provided that all the documentary requirements are complied with.

The following documents shall form part of the contract:

      - Contract Agreement;

      - Bidding Documents;

      - Winning Bidder’s bid, including the Technical and Financial Proposals, and all other documents/statements submitted (e.g., Bidder’s response to request for clarifications on the bid), including corrections to the bid, if any, resulting from the Procuring Entity’s bid evaluation;

      - Performance Security;

      - Notice of Award of Contract; and

      - Other contract documents that may be required by existing laws and/or specified in the BDS.

### Performance Security

To guarantee the faithful performance by the winning Bidder of its obligations under the contract, it shall post a performance security within a maximum period of ten (10) calendar days from the receipt of the Notice of Award from the Procuring Entity and in no case later than the signing of the contract.

The Performance Security shall be denominated in Philippine Pesos and posted in favor of the Procuring Entity in an amount not less than the percentage of the total contract price in accordance with the following schedule:

| Form of Performance Security | Amount of Performance Security (Not less than the Percentage of the Total Contract Price) |
| --- | --- |
| Cash or cashier’s/manager’s check issued by a Universal or Commercial Bank. For biddings conducted by the LGUs, the Cashier’s/Manager’s Check may be issued by other banks certified by the BSP as authorized to issue such financial instrument. | Ten percent (10%) |
| Bank draft/guarantee or irrevocable letter of credit issued by a Universal or Commercial Bank: Provided, however, that it shall be confirmed or authenticated by a Universal or Commercial Bank, if issued by a foreign bank. For biddings conducted by the LGUs, Bank Draft/Guarantee, or Irrevocable Letter of Credit may be issued by other banks certified by the BSP as authorized to issue such financial instrument. |  |
| Surety bond callable upon demand issued by a surety or insurance company duly certified by the Insurance Commission as authorized to issue such security. | Thirty percent (30%) |

Failure of the successful Bidder to comply with the above-mentioned requirement shall constitute sufficient ground for the annulment of the award and forfeiture of the bid security, in which event the Procuring Entity shall have a fresh period to initiate and complete the post qualification of the second Lowest Calculated Bid. The procedure shall be repeated until LCRB is identified and selected for recommendation of contract award. However if no Bidder passed post-qualification, the BAC shall declare the bidding a failure and conduct a re-bidding with re-advertisement, if necessary.

### Notice to Proceed

Within seven (7) calendar days from the date of approval of the Contract by the appropriate government approving authority, the Procuring Entity shall issue the Notice to Proceed (NTP) together with a copy or copies of the approved contract to the successful Bidder. All notices called for by the terms of the contract shall be effective only at the time of receipt thereof by the successful Bidder.

### Protest Mechanism

Decision of the procuring entity at any stage of the procurement process may be questioned in accordance with Sections 55 of the IRR of RA 9184.

# Section III. Bid Data Sheet

Notes on the Bid Data Sheet This Section is intended to assist the Procuring Entity in providing the specific information in relation to corresponding clauses in the ITB included in Section II, and has to be prepared for each specific procurement. The Procuring Entity should specify in the BDS information and requirements specific to the circumstances of the Procuring Entity, the processing of the procurement, the applicable rules regarding bid price and currency, and the bid evaluation criteria that will apply to the Bids. In preparing this Section, the following aspects should be checked: (a) Information that specifies and complements provisions of Section II. Instructions to Bidders must be incorporated. (b) Amendments and/or supplements, if any, to provisions of Section II. Instructions to Bidders as necessitated by the circumstances of the specific procurement, must also be incorporated. For foreign-assisted projects, the Bid Data Sheet to be used is provided in Section X-Foreign-Assisted Projects.

Bid Data Sheet

| ITB Clause |  |
| --- | --- |
| 1.1 | The Procuring Entity is Philippine Ports Authority, PMO-Panay/Guimaras The name of the Contract is “Repair of Passenger Terminal Building of Port of Estancia, Iloilo”. The identification number of the Contract is A170123. |
| 2 | The Funding Source is: The Government of the Philippines (GoP) through [indicate source of funding and year] in the amount of [insert amount of funds]. NOTE: In the case of National Government Agencies, the General Appropriations Act and/or continuing appropriations; in the case of Government-Owned and/or –Controlled Corporations, Government Financial Institutions, and State Universities and Colleges, the Corporate Budget for the contract approved by the governing Boards; in the case of Local Government Units, the Budget for the contract approved by the respective Sanggunian. The name of the Project is “Repair of Passenger Terminal Building of Port of Estancia, Iloilo” |
| 3.1 | No further instructions. |
| 5.1 | No further instructions. |
| 5.2 | Select one, delete the other. Foreign bidders may participate in this Project as provided for in [State relevant provisions of the applicable Treaty or International or Executive Agreement.] or Bidding is restricted to eligible bidders as defined in ITB Clause 5.1. |
| 5.4(a) | No further instructions. |
| 5.4(b) | For this purpose, similar contracts shall refer to contracts which have the same major categories of work. [insert description/clarification of what are major categories of work]. |
| 8.1 | State either “Subcontracting is not allowed.” or specify the portions of Works and the maximum percentage allowed to be subcontracted. NOTE: The contractor shall undertake not less than 50% of the contracted works with its own resources. |
| 8.2 | If subcontracting is allowed, specify the eligibility criteria that subcontractors must comply with; including the corresponding documentary requirements therefor; otherwise, state “Not applicable.” |
| 9.1 | The Procuring Entity will hold a pre-bid conference for this Project on August 16, 2017 at 10:00 A.M at the PPA Conference Room, 2nd Floor, Admin. Bldg., ICPC, Iloilo City. |
| 10.1 | The Procuring Entity’s address is: Brgy. Loboc, La Paz, Iloilo City Engr. Rona Mae B. Barabona, BAC Secretariat (033) 337-7791 local 302-303 esd_pmoiloilo@yahoo.com |
| 10.4 | No further instructions. |
| 12.1 | No further instructions. |
| 12.1(a)(iii) | No further instructions. |
| 12.1(b)(ii.2) | The minimum work experience requirements for key personnel are the following: Key Personnel General Experience Relevant Experience Project Manager Project Engineer Materials Engineer Construction Safety & Health Officer Foreman |
| 12.1(b)(iii.3) | The minimum major equipment requirements are the following: Equipment Capacity Number of Units Grinder/Tile Cutter 2 Stake Truck 1 Electric Cutter 1 Oxy-cutting outfit 1 |
| 13.1 | List any additional requirements or state “No additional Requirements” |
| 13.1(b) | This shall include all of the following documents: Bid prices in the Bill of Quantities; Detailed estimates, including a summary sheet indicating the unit prices of construction materials, labor rates, and equipment rentals used in coming up with the Bid; and Cash flow by quarter or payment schedule. |
| 13.2 | The ABC is Five Million, Nine Hundred Forty Six Thousand, Two Hundred Two Pesos and 93/100 (P5, 946, 202.93). Any bid with a financial component exceeding this amount shall not be accepted. |
| 14.2 | Insert value engineering clause if allowed, otherwise state “No further instructions.” |
| 15.4 | No further instruction. |
| 16.1 | Select one, delete the other: The bid prices shall be quoted in Philippine Pesos. |
| 16.3 | No further instructions. |
| 17.1 | Bids will be valid until 120 calendar days from the date of the opening of bids. |
| 18.1 | The bid security shall be in the form of a Bid Securing Declaration or any of the following forms and amounts: The amount of not less than One Hundred Eighteen Thousand Nine Hundred Twenty-Four Pesos and 06/100 (118,924.06) [2% of ABC], if bid security is in cash, cashier’s/manager’s check, bank draft/guarantee or irrevocable letter of credit; The amount of not less than Two Hundred Ninety Seven Thousand Three Hundred Ten Pesos and 15/100 (P 297,310.15) [5% of ABC] if bid security is in Surety Bond. |
| 18.2 | The bid security shall be valid until 120 calendar days from the date of the opening of bids. |
| 20.3 | Each Bidder shall submit one (1) original and two (2) copies of the first and second components of its bid. |
| 21 | The address for submission of bids is PPA Conference Room, 2rd Floor, Admin. Bldg., ICPC, Iloilo City. The deadline for submission of bids is August 29, 2017; 8:30 A.M. |
| 24.1 | The place of bid opening is PPA Conference Room, 2rd Floor, Admin. Bldg., ICPC, Iloilo City. The date and time of bid opening is August 29, 2017;09:00 A.M. |
| 24.2 | No further instructions. |
| 24.3 | No further instructions. |
| 27.3 | Select one of the following paragraphs and delete the other: Partial bid is not allowed. The infrastructure project is packaged in a single lot and the lot shall not be divided into sub-lots for the purpose of bidding, evaluation, and contract award. In all cases, the NFCC computation, if applicable, must be sufficient for all the lots or contracts to be awarded to the Bidder. [Insert grouping of lots] |
| 27.4 | No further instructions. |
| 28.2 | List licenses and permits relevant to the Project and the corresponding law requiring it or state “None.” |
| 31.4(f) | List additional contract documents relevant to the Project that may be required by existing laws and/or the Procuring Entity, such as construction schedule and S-curve, manpower schedule, construction methods, equipment utilization schedule, construction safety and health program approved by the Department of Labor and Employment, and PERT/CPM or other acceptable tools of project scheduling. |

# Section IV. General Conditions of Contract

Notes on the General Conditions of Contract The GCC in Section IV, read in conjunction with the SCC in Section V and other documents listed therein, should be a complete document expressing all the rights and obligations of the parties. The GCC herein shall not be altered. Any changes and complementary information, which may be needed, shall be introduced only through the SCC in Section V.

TABLE OF CONTENTS

1.	Definitions	49

2.	Interpretation	51

3.	Governing Language and Law	52

4.	Communications	52

5.	Possession of Site	52

6.	The Contractor’s Obligations	53

7.	Performance Security	54

8.	Subcontracting	55

9.	Liquidated Damages	55

10.	Site Investigation Reports	55

11.	The Procuring Entity, Licenses and Permits	55

12.	Contractor’s Risk and Warranty Security	56

13.	Liability of the Contractor	58

14.	Procuring Entity’s Risk	58

15.	Insurance	58

16.	Termination for Default of Contractor	60

17.	Termination for Default of Procuring Entity	60

18.	Termination for Other Causes	61

19.	Procedures for Termination of Contracts	62

20.	Force Majeure, Release From Performance	65

21.	Resolution of Disputes	65

22.	Suspension of Loan, Credit, Grant, or Appropriation	66

23.	Procuring Entity’s Representative’s Decisions	66

24.	Approval of Drawings and Temporary Works by the Procuring Entity’s Representative	66

25.	Acceleration and Delays Ordered by the Procuring Entity’s Representative	67

26.	Extension of the Intended Completion Date	67

27.	Right to Vary	67

28.	Contractors Right to Claim	68

29.	Dayworks	68

30.	Early Warning	68

31.	Program of Work	68

32.	Management Conferences	69

33.	Bill of Quantities	69

34.	Instructions, Inspections and Audits	70

35.	Identifying Defects	70

36.	Cost of Repairs	70

37.	Correction of Defects	70

38.	Uncorrected Defects	71

39.	Advance Payment	71

40.	Progress Payments	71

41.	Payment Certificates	72

42.	Retention	72

43.	Variation Orders	73

44.	Contract Completion	75

45.	Suspension of Work	75

46.	Payment on Termination	76

47.	Extension of Contract Time	76

48.	Price Adjustment	77

49.	Completion	78

50.	Taking Over	78

51.	Operating and Maintenance Manuals	78

### Definitions

For purposes of this Clause, boldface type is used to identify defined terms.

The Arbiter is the person appointed jointly by the Procuring Entity and the Contractor to resolve disputes in the first instance, as provided for in GCC Clause 21.

Bill of Quantities refers to a list of the specific items of the Work and their corresponding unit prices, lump sums, and/or provisional sums.

The Completion Date is the date of completion of the Works as certified by the Procuring Entity’s Representative, in accordance with GCC Clause 49.

The Contract is the contract between the Procuring Entity and the Contractor to execute, complete, and maintain the Works.

  - The Contract Effectivity Date is the date of signing of the Contract.  However, the contractor shall commence execution of the Works on the Start Date as defined in GCC Clause 1.28.

  - The Contract Price is the price stated in the Notice of Award and thereafter to be paid by the Procuring Entity to the Contractor for the execution of the Works in accordance with this Contract

  - Contract Time Extension is the allowable period for the Contractor to complete the Works in addition to the original Completion Date stated in this Contract.

1.8 	The Contractor is the juridical entity whose proposal has been accepted by the Procuring Entity and to whom the Contract to execute the Work was awarded.

1.9 	The Contractor’s Bid is the signed offer or proposal submitted by the Contractor to the Procuring Entity in response to the Bidding Documents.

1.10	Days are calendar days; months are calendar months.

  - Dayworks are varied work inputs subject to payment on a time basis for the Contractor’s employees and Equipment, in addition to payments for associated Materials and Plant.

1.12	A Defect is any part of the Works not completed in accordance with the Contract.

1.13 	The Defects Liability Certificate is the certificate issued by Procuring Entity’s Representative upon correction of defects by the Contractor.

  - The Defects Liability Period is the one year period between contract completion and final acceptance within which the Contractor assumes the responsibility to undertake the repair of any damage to the Works at his own expense.

1.15	Drawings are graphical presentations of the Works. They include all supplementary details, shop drawings, calculations, and other information provided or approved for the execution of this Contract.

1.16	Equipment refers to all facilities, supplies, appliances, materials or things required for the execution and completion of the Work provided by the Contractor and which shall not form or are not intended to form part of the Permanent Works.

  - The Intended Completion Date refers to the date specified in the SCC when the Contractor is expected to have completed the Works.  The Intended Completion Date may be revised only by the Procuring Entity’s Representative by issuing an extension of time or an acceleration order.

1.18	Materials are all supplies, including consumables, used by the Contractor for incorporation in the Works.

1.19	The Notice to Proceed is a written notice issued by the Procuring Entity or the Procuring Entity’s Representative to the Contractor requiring the latter to begin the commencement of the work not later than a specified or determinable date.

  - Permanent Works are all permanent structures and all other project features and facilities required to be constructed and completed in accordance with this Contract which shall be delivered to the Procuring Entity and which shall remain at the Site after the removal of all Temporary Works.

1.21	Plant refers to the machinery, apparatus, and the like intended to form an integral part of the Permanent Works.

1.22	The Procuring Entity is the party who employs the Contractor to carry out the Works stated in the SCC.

  - The Procuring Entity’s Representative refers to the Head of the Procuring Entity or his duly authorized representative, identified in the SCC, who shall be responsible for supervising the execution of the Works and administering this Contract.

1.24 	The Site is the place provided by the Procuring Entity where the Works shall be executed and any other place or places which may be designated in the SCC, or notified to the Contractor by the Procuring Entity’s Representative as forming part of the Site.

1.25 	Site Investigation Reports are those that were included in the Bidding Documents and are factual and interpretative reports about the surface and subsurface conditions at the Site.

1.26 	Slippage is a delay in work execution occurring when actual accomplishment falls below the target as measured by the difference between the scheduled and actual accomplishment of the Work by the Contractor as established from the work schedule. This is actually described as a percentage of the whole Works.

  - Specifications means the description of Works to be done and the qualities of materials to be used, the equipment to be installed and the mode of construction.

1.28 	The Start Date, as specified in the SCC, is the date when the Contractor is obliged to commence execution of the Works.  It does not necessarily coincide with any of the Site Possession Dates.

1.29 	A Subcontractor is any person or organization to whom a part of the Works has been subcontracted by the Contractor, as allowed by the Procuring Entity, but not any assignee of such person.

1.30	Temporary Works are works designed, constructed, installed, and removed by the Contractor that are needed for construction or installation of the Permanent Works.

  - Work(s) refer to the Permanent Works and Temporary Works to be executed by the Contractor in accordance with this Contract, including (i) the furnishing of all labor, materials, equipment and others incidental, necessary or convenient to the complete execution of the Works; (ii) the passing of any tests before acceptance by the Procuring Entity’s Representative; (iii) and the carrying out of all duties and obligations of the Contractor imposed by this Contract as described in the SCC.

### Interpretation

In interpreting the Conditions of Contract, singular also means plural, male also means female or neuter, and the other way around.  Headings have no significance.  Words have their normal meaning under the language of this Contract unless specifically defined.  The Procuring Entity’s Representative will provide instructions clarifying queries about the Conditions of Contract.

If sectional completion is specified in the SCC, references in the Conditions of Contract to the Works, the Completion Date, and the Intended Completion Date apply to any Section of the Works (other than references to the Completion Date and Intended Completion Date for the whole of the Works).

The documents forming this Contract shall be interpreted in the following order of priority:

- Contract Agreement;

- Bid Data Sheet;

- Instructions to Bidders;

- Addenda to the Bidding Documents;

- Special Conditions of Contract;

- General Conditions of Contract;

- Specifications;

- Bill of Quantities; and

- Drawings.

### Governing Language and Law

This Contract has been executed in the English language, which shall be the binding and controlling language for all matters relating to the meaning or interpretation of this Contract.  All correspondence and other documents pertaining to this Contract which are exchanged by the parties shall be written in English.

This Contract shall be interpreted in accordance with the laws of the Republic of the Philippines.

### Communications

Communications between parties that are referred to in the Conditions shall be effective only when in writing.  A notice shall be effective only when it is received by the concerned party.

### Possession of Site

On the date specified in the SCC, the Procuring Entity shall grant the Contractor possession of so much of the Site as may be required to enable it to proceed with the execution of the Works. If the Contractor suffers delay or incurs cost from failure on the part of the Procuring Entity to give possession in accordance with the terms of this clause, the Procuring Entity’s Representative shall give the Contractor a Contract Time Extension and certify such sum as fair to cover the cost incurred, which sum shall be paid by Procuring Entity.

If possession of a portion is not given by the date stated in the SCC Clause 5.1, the Procuring Entity will be deemed to have delayed the start of the relevant activities.  The resulting adjustments in contract time to address such delay shall be in accordance with GCC Clause 47.

The Contractor shall bear all costs and charges for special or temporary right-of-way required by it in connection with access to the Site. The Contractor shall also provide at his own cost any additional facilities outside the Site required by it for purposes of the Works.

The Contractor shall allow the Procuring Entity’s Representative and any person authorized by the Procuring Entity’s Representative access to the Site and to any place where work in connection with this Contract is being carried out or is intended to be carried out.

### The Contractor’s Obligations

The Contractor shall carry out the Works properly and in accordance with this Contract. The Contractor shall provide all supervision, labor, Materials, Plant and Contractor's Equipment, which may be required. All Materials and Plant on Site shall be deemed to be the property of the Procuring Entity.

The Contractor shall commence execution of the Works on the Start Date and shall carry out the Works in accordance with the Program of Work submitted by the Contractor, as updated with the approval of the Procuring Entity’s Representative, and complete them by the Intended Completion Date.

The Contractor shall be responsible for the safety of all activities on the Site.

The Contractor shall carry out all instructions of the Procuring Entity’s Representative that comply with the applicable laws where the Site is located.

The Contractor shall employ the key personnel named in the Schedule of Key Personnel, as referred to in the SCC, to carry out the supervision of the Works. The Procuring Entity will approve any proposed replacement of key personnel only if their relevant qualifications and abilities are equal to or better than those of the personnel listed in the Schedule.

If the Procuring Entity’s Representative asks the Contractor to remove a member of the Contractor’s staff or work force, for justifiable cause, the Contractor shall ensure that the person leaves the Site within seven (7) days and has no further connection with the Work in this Contract.

During Contract implementation, the Contractor and his subcontractors shall abide at all times by all labor laws, including child labor related enactments, and other relevant rules.

The Contractor shall submit to the Procuring Entity for consent the name and particulars of the person authorized to receive instructions on behalf of the Contractor.

The Contractor shall cooperate and share the Site with other contractors, public authorities, utilities, and the Procuring Entity between the dates given in the schedule of other contractors particularly when they shall require access to the Site.  The Contractor shall also provide facilities and services for them during this period.  The Procuring Entity may modify the schedule of other contractors, and shall notify the Contractor of any such modification thereto.

Should anything of historical or other interest or of significant value be unexpectedly discovered on the Site, it shall be the property of the Procuring Entity.  The Contractor shall notify the Procuring Entity’s Representative of such discoveries and carry out the Procuring Entity’s Representative’s instructions in dealing with them.

### Performance Security

Within ten (10) calendar days from receipt of the Notice of Award from the Procuring Entity but in no case later than the signing of the contract by both parties, the Contractor shall furnish the performance security in any of the forms prescribed in ITB Clause 32.2.

The performance security posted in favor of the Procuring Entity shall be forfeited in the event it is established that the Contractor is in default in any of its obligations under the Contract.

The performance security shall remain valid until issuance by the Procuring Entity of the Certificate of Final Acceptance.

The performance security may be released by the Procuring Entity and returned to the Contractor after the issuance of the Certificate of Final Acceptance subject to the following conditions:

      - There are no pending claims against the Contractor or the surety company filed by the Procuring Entity;

      - The Contractor has no pending claims for labor and materials filed against it; and

      - Other terms specified in the SCC.

The Contractor shall post an additional performance security following the amount and form specified in ITB Clause 32.2 to cover any cumulative increase of more than ten percent (10%) over the original value of the contract as a result of amendments to order or change orders, extra work orders and supplemental agreements, as the case may be.  The Contractor shall cause the extension of the validity of the performance security to cover approved contract time extensions.

In case of a reduction in the contract value or for partially completed Works under the contract which are usable and accepted by the Procuring Entity the use of which, in the judgment of the implementing agency or the Procuring Entity, will not affect the structural integrity of the entire project, the Procuring Entity shall allow a proportional reduction in the original performance security, provided that any such reduction is more than ten percent (10%) and that the aggregate of such reductions is not more than fifty percent (50%) of the original performance security.

Unless otherwise indicated in the SCC, the Contractor, by entering into the Contract with the Procuring Entity, acknowledges the right of the Procuring Entity to institute action pursuant to  Act 3688 against any subcontractor be they an individual, firm, partnership, corporation, or association supplying the Contractor with labor, materials and/or equipment for the performance of this Contract.

### Subcontracting

Unless otherwise indicated in the SCC, the Contractor cannot subcontract Works more than the percentage specified in BDS Clause 8.1.

Subcontracting of any portion of the Works does not relieve the Contractor of any liability or obligation under this Contract.  The Contractor will be responsible for the acts, defaults, and negligence of any subcontractor, its agents, servants or workmen as fully as if these were the Contractor’s own acts, defaults, or negligence, or those of its agents, servants or workmen.

If subcontracting is allowed. The contractor may identify its subcontractor during contract implementation stage. Subcontractors disclosed and identified during the bidding may be changed during the implementation of this Contract. In either case, subcontractors must submit the documentary requirements under ITB Clause 12 and comply with the eligibility criteria specified in the BDS. In the event that any subcontractor is found by any Procuring Entity to be eligible, the subcontracting of such portion of the Works shall be disallowed.

### Liquidated Damages

The Contractor shall pay liquidated damages to the Procuring Entity for each day that the Completion Date is later than the Intended Completion Date.  The applicable liquidated damages is at least one-tenth (1/10) of a percent of the cost of the unperformed portion for every day of delay.  The total amount of liquidated damages shall not exceed ten percent (10%) of the amount of the contract.  The Procuring Entity may deduct liquidated damages from payments due to the Contractor.  Payment of liquidated damages shall not affect the Contractor’s liabilities. Once the cumulative amount of liquidated damages reaches ten percent (10%) of the amount of this Contract, the Procuring Entity may rescind or terminate this Contract, without prejudice to other courses of action and remedies available under the circumstances.

If the Intended Completion Date is extended after liquidated damages have been paid, the Engineer of the Procuring Entity shall correct any overpayment of liquidated damages by the Contractor by adjusting the next payment certificate.

### Site Investigation Reports

The Contractor, in preparing the Bid, shall rely on any Site Investigation Reports referred to in the SCC supplemented by any information obtained by the Contractor.

### The Procuring Entity, Licenses and Permits

The Procuring Entity shall, if requested by the Contractor, assist him in applying for permits, licenses or approvals, which are required for the Works.

### Contractor’s Risk and Warranty Security

The Contractor shall assume full responsibility for the Works from the time project construction commenced up to final acceptance by the Procuring Entity and shall be held responsible for any damage or destruction of the Works except those occasioned by force majeure. The Contractor shall be fully responsible for the safety, protection, security, and convenience of his personnel, third parties, and the public at large, as well as the Works, Equipment, installation, and the like to be affected by his construction work.

The defects liability period for infrastructure projects shall be one year from contract completion up to final acceptance by the Procuring Entity.  During this period, the Contractor shall undertake the repair works, at his own expense, of any damage to the Works on account of the use of materials of inferior quality within ninety (90) days from the time the HoPE has issued an order to undertake repair.  In case of failure or refusal to comply with this mandate, the Procuring Entity shall undertake such repair works and shall be entitled to full reimbursement of expenses incurred therein upon demand.

Unless otherwise indicated in the SCC, in case the Contractor fails to comply with the preceding paragraph, the Procuring Entity shall forfeit its performance security, subject its property(ies) to attachment or garnishment proceedings, and perpetually disqualify it from participating in any public bidding. All payables of the GoP in his favor shall be offset to recover the costs.

After final acceptance of the Works by the Procuring Entity, the Contractor shall be held responsible for “Structural Defects,” i.e., major faults/flaws/deficiencies in one or more key structural elements of the project which may lead to structural 	failure of the completed elements or structure, or “Structural Failures,” i.e., where one or more key structural elements in an infrastructure facility fails or collapses, thereby rendering the facility or part thereof incapable of withstanding the design loads, and/or endangering the safety of the users or the general public:

      - Contractor – Where Structural Defects/Failures arise due to faults attributable to improper construction, use of inferior quality/substandard materials, and any violation of the contract plans and specifications, the contractor shall be held liable;

      - Consultants – Where Structural Defects/Failures arise due to faulty and/or inadequate design and specifications as well as construction supervision, then the consultant who prepared the design or undertook construction supervision for the project shall be held liable;

      - Procuring Entity’s Representatives/Project Manager/Construction Managers and Supervisors – The project owner’s representative(s), project manager, construction manager, and supervisor(s) shall be held liable in cases where the Structural Defects/Failures are due to his/their willful intervention in altering the designs and other specifications; negligence or omission in not approving or acting on proposed changes to noted defects or deficiencies in the design and/or specifications; and the use of substandard construction materials in the project;

      - Third Parties - Third Parties shall be held liable in cases where Structural Defects/Failures are caused by work undertaken by them such as leaking pipes, diggings or excavations, underground cables and electrical wires, underground tunnel, mining shaft and the like, in which case the applicable warranty to such structure should be levied to third parties for their construction or restoration works.

      - Users - In cases where Structural Defects/Failures are due to abuse/misuse by the end user of the constructed facility and/or non–compliance by a user with the technical design limits and/or intended purpose of the same, then the user concerned shall be held liable.

The warranty against Structural Defects/Failures, except those occasioned on force majeure, shall cover the period specified in the SCC reckoned from the date of issuance of the Certificate of Final Acceptance by the Procuring Entity.

The Contractor shall be required to put up a warranty security in the form of cash, bank guarantee, letter of credit, GSIS or surety bond callable on demand, in accordance with the following schedule:

| Form of Warranty | Amount of Warranty Security Not less than the Percentage (%) of Total Contract Price |
| --- | --- |
| Cash or letter of credit issued by Universal or Commercial bank: provided, however, that the letter of credit shall be confirmed or authenticated by a Universal or Commercial bank, if issued by a foreign bank | Five Percent (5%) |
| Bank guarantee confirmed by Universal or Commercial bank: provided, however, that the letter of credit shall be confirmed or authenticated by a Universal or Commercial bank, if issued by a foreign bank | Ten Percent (10%) |
| Surety bond callable upon demand issued by GSIS or any surety or insurance company duly certified by the Insurance Commission | Thirty Percent (30%) |

The warranty security shall be stated in Philippine Pesos and shall remain effective for one year from the date of issuance of the Certificate of Final Acceptance by the Procuring Entity, and returned only after the lapse of said one year period.

In case of structural defects/failure occurring during the applicable warranty period provided in GCC Clause 12.5, the Procuring Entity shall undertake the necessary restoration or reconstruction works and shall be entitled to full reimbursement by the parties found to be liable for expenses incurred therein upon demand, without prejudice to the filing of appropriate administrative, civil, and/or criminal charges against the responsible persons as well as the forfeiture of the warranty security posted in favor of the Procuring Entity.

### Liability of the Contractor

Subject to additional provisions, if any, set forth in the SCC, the Contractor’s liability under this Contract shall be as provided by the laws of the Republic of the Philippines.

### Procuring Entity’s Risk

From the Start Date until the Certificate of Final Acceptance has been issued, the following are risks of the Procuring Entity:

      - The risk of personal injury, death, or loss of or damage to property (excluding the Works, Plant, Materials, and Equipment), which are due to:

        - any type of use or occupation of the Site authorized by the Procuring Entity after the official acceptance of the works; or

        - negligence, breach of statutory duty, or interference with any legal right by the Procuring Entity or by any person employed by or contracted to him except the Contractor.

      - The risk of damage to the Works, Plant, Materials, and Equipment to the extent that it is due to a fault of the Procuring Entity or in the Procuring Entity’s design, or due to war or radioactive contamination directly affecting the country where the Works are to be executed.

### Insurance

The Contractor shall, under his name and at his own expense, obtain and maintain, for the duration of this Contract, the following insurance coverage:

      - Contractor’s All Risk Insurance;

      - Transportation to the project Site of Equipment, Machinery, and Supplies owned by the Contractor;

      - Personal injury or death of Contractor’s employees; and

      - Comprehensive insurance for third party liability to Contractor’s direct or indirect act or omission causing damage to third persons.

The Contractor shall provide evidence to the Procuring Entity’s Representative that the insurances required under this Contract have been effected and shall, within a reasonable time, provide copies of the insurance policies to the Procuring Entity’s Representative.  Such evidence and such policies shall be provided to the Procuring Entity’s through the Procuring Entity’s Representative.

The Contractor shall notify the insurers of changes in the nature, extent, or program for the execution of the Works and ensure the adequacy of the insurances at all times in accordance with the terms of this Contract and shall produce to the Procuring Entity’s Representative the insurance policies in force including the receipts for payment of the current premiums.

The above insurance policies shall be obtained from any reputable insurance company approved by the Procuring Entity’s Representative.

If the Contractor fails to obtain and keep in force the insurances referred to herein or any other insurance which he may be required to obtain under the terms of this Contract, the Procuring Entity may obtain and keep in force any such insurances and pay such premiums as may be necessary for the purpose.  From time to time, the Procuring Entity may deduct the amount it shall pay for said premiums including twenty five percent (25%) therein from any monies due, or which may become due, to the Contractor, without prejudice to the Procuring Entity exercising its right to impose other sanctions against the Contractor pursuant to the provisions of this Contract.

In the event the Contractor fails to observe the above safeguards, the Procuring Entity may, at the Contractor’s expense, take whatever measure is deemed necessary for its protection and that of the Contractor’s personnel and third parties, and/or order the interruption of dangerous Works.  In addition, the Procuring Entity may refuse to make the payments under GCC Clause 40 until the Contractor complies with this Clause.

The Contractor shall immediately replace the insurance policy obtained as required in this Contract, without need of the Procuring Entity’s demand, with a new policy issued by a new insurance company acceptable to the Procuring Entity for any of the following grounds:

      - The issuer of the insurance policy to be replaced has:

        - become bankrupt;

        - been placed under receivership or under a management committee;

        - been sued for suspension of payment; or

        - been suspended by the Insurance Commission and its license to engage in business or its authority to issue insurance policies cancelled; or

        - Where reasonable grounds exist that the insurer may not be able, fully and promptly, to fulfill its obligation under the insurance policy.

### Termination for Default of Contractor

The Procuring Entity shall terminate this Contract for default when any of the following conditions attend its implementation:

        - Due to the Contractor’s fault and while the project is on-going, it has incurred negative slippage of fifteen percent (15%) or more in accordance with Presidential Decree 1870, regardless of whether or not previous warnings and notices have been issued for the Contractor to improve his performance;

        - Due to its own fault and after this Contract time has expired, the Contractor incurs delay in the completion of the Work after this Contract has expired; or

        - The Contractor:

              - abandons the contract Works, refuses or fails to comply with a valid instruction of the Procuring Entity or fails to proceed expeditiously and without delay despite a written notice by the Procuring Entity;

              - does not actually have on the project Site the minimum essential equipment listed on the bid necessary to prosecute the Works in accordance with the approved Program of Work and equipment deployment schedule as required for the project;

              - does not execute the Works in accordance with this Contract or persistently or flagrantly neglects to carry out its obligations under this Contract;

              - neglects or refuses to remove materials or to perform a new Work that has been rejected as defective or unsuitable; or

              - sub-lets any part of this Contract without approval by the Procuring Entity.

All materials on the Site, Plant, Works, including Equipment purchased and funded under the Contract shall be deemed to be the property of the Procuring Entity if this Contract is rescinded because of the Contractor’s default.

### Termination for Default of Procuring Entity

The Contractor may terminate this Contract with the Procuring Entity if the works are completely stopped for a continuous period of at least sixty (60) calendar days through no fault of its own, due to any of the following reasons:

      - Failure of the Procuring Entity to deliver, within a reasonable time, supplies, materials, right-of-way, or other items it is obligated to furnish under the terms of this Contract; or

      - The prosecution of the Work is disrupted by the adverse peace and order situation, as certified by the Armed Forces of the Philippines Provincial Commander and approved by the Secretary of National Defense.

### Termination for Other Causes

The Procuring Entity may terminate this Contract, in whole or in part, at any time for its convenience.  The HoPE may terminate this Contract for the convenience of the Procuring Entity if he has determined the existence of conditions that make Project Implementation economically, financially or technically impractical and/or unnecessary, such as, but not limited to, fortuitous event(s) or changes in law and National Government policies.

The Procuring Entity or the Contractor may terminate this Contract if the other party causes a fundamental breach of this Contract.

Fundamental breaches of Contract shall include, but shall not be limited to, the following:

      - The Contractor stops work for twenty eight (28) days when no stoppage of work is shown on the current Program of Work and the stoppage has not been authorized by the Procuring Entity’s Representative;

      - The Procuring Entity’s Representative instructs the Contractor to delay the progress of the Works, and the instruction is not withdrawn within twenty eight (28) days;

      - The Procuring Entity shall terminate this Contract if the Contractor is declared bankrupt or insolvent as determined with finality by a court of competent jurisdiction.  In this event, termination will be without compensation to the Contractor, provided that such termination will not prejudice or affect any right of action or remedy which has accrued or will accrue thereafter to the Procuring Entity and/or the Contractor.  In the case of the Contractor's insolvency, any Contractor's Equipment which the Procuring Entity instructs in the notice is to be used until the completion of the Works;

      - A payment certified by the Procuring Entity’s Representative is not paid by the Procuring Entity to the Contractor within eighty four (84) days from the date of the Procuring Entity’s Representative’s certificate;

      - The Procuring Entity’s Representative gives Notice that failure to correct a particular Defect is a fundamental breach of Contract and the Contractor fails to correct it within a reasonable period of time determined by the Procuring Entity’s Representative;

      - The Contractor does not maintain a Security, which is required;

      - The Contractor has delayed the completion of the Works by the number of days for which the maximum amount of liquidated damages can be paid, as defined in the GCC Clause 9; and

      - In case it is determined prima facie by the Procuring Entity that the Contractor has engaged, before or during the implementation of the contract, in unlawful deeds and behaviors relative to contract acquisition and implementation, such as, but not limited to, the following:

        - corrupt, fraudulent, collusive, coercive, and obstructive  practices as defined in ITB Clause 3.1(a), unless otherwise specified in the SCC;

        - drawing up or using forged documents;

        - using adulterated materials, means or methods, or engaging in production contrary to rules of science or the trade; and

        - any other act analogous to the foregoing.

The Funding Source or the Procuring Entity, as appropriate, will seek to impose the maximum civil, administrative and/or criminal penalties available under the applicable law on individuals and organizations deemed to be involved with corrupt, fraudulent, or coercive practices.

When persons from either party to this Contract gives notice of a fundamental breach to the Procuring Entity’s Representative  in order to terminate the existing contract for a cause other than those listed under GCC Clause 18.3, the Procuring Entity’s Representative shall decide whether the breach is fundamental or not.

If this Contract is terminated, the Contractor shall stop work immediately, make the Site safe and secure, and leave the Site as soon as reasonably possible.

### Procedures for Termination of Contracts

The following provisions shall govern the procedures for the termination of this Contract:

      - Upon receipt of a written report of acts or causes which may constitute ground(s) for termination as aforementioned, or upon its own initiative, the Procuring Entity shall, within a period of seven (7) calendar days, verify the existence of such ground(s) and cause the execution of a Verified Report, with all relevant evidence attached;

      - Upon recommendation by the Procuring Entity, the HoPE shall terminate this Contract only by a written notice to the Contractor conveying the termination of this Contract. The notice shall state:

        - that this Contract is being terminated for any of the ground(s) afore-mentioned, and a statement of the acts that constitute the ground(s) constituting the same;

        - the extent of termination, whether in whole or in part;

        - an instruction to the Contractor to show cause as to why this Contract should not be terminated; and

        - special instructions of the Procuring Entity, if any.

The Notice to Terminate shall be accompanied by a copy of the Verified Report;

      - Within a period of seven (7) calendar days from receipt of the Notice of Termination, the Contractor shall submit to the HoPE a verified position paper stating why the contract should not be terminated.  If the Contractor fails to show cause after the lapse of the seven (7) day period, either by inaction or by default, the HoPE shall issue an order terminating the contract;

      - The Procuring Entity may, at anytime before receipt of the Contractor’s verified position paper described in item (c) above withdraw the Notice to Terminate if it is determined that certain items or works subject of the notice had been completed, delivered, or performed before the Contractor’s receipt of the notice;

      - Within a non-extendible period of ten (10) calendar days from receipt of the verified position paper, the HoPE shall decide whether or not to terminate this Contract.  It shall serve a written notice to the Contractor of its decision and, unless otherwise provided in the said notice, this Contract is deemed terminated from receipt of the Contractor of the notice of decision.  The termination shall only be based on the ground(s) stated in the Notice to Terminate; and

      - The HoPE may create a Contract Termination Review Committee (CTRC) to assist him in the discharge of this function.  All decisions recommended by the CTRC shall be subject to the approval of the HoPE.

Pursuant to Section 69(f) of RA 9184 and without prejudice to the imposition of additional administrative sanctions as the internal rules of the agency may provide and/or further criminal prosecution as provided by applicable laws, the procuring entity shall impose on contractors after the termination of the contract the penalty of suspension for one (1) year for the first offense, suspension for two (2) years for the second offense from participating in the public bidding process, for violations committed during the contract implementation stage, which include but not limited to the following:

      - Failure of the contractor, due solely to his fault or negligence, to mobilize and start work or performance within the specified period in the Notice to Proceed (“NTP”);

      - Failure by the contractor to fully and faithfully comply with its contractual obligations without valid cause, or failure by the contractor to comply with any written lawful instruction of the procuring entity or its representative(s) pursuant to the implementation of the contract.  For the procurement of infrastructure projects or consultancy contracts, lawful instructions include but are not limited to the following:

        - Employment of competent technical personnel, competent engineers and/or work supervisors;

        - Provision of warning signs and barricades in accordance with approved plans and specifications and contract provisions;

        - Stockpiling in proper places of all materials and removal from the project site of waste and excess materials, including broken pavement and excavated debris in accordance with approved plans and specifications and contract provisions;

        - Deployment of committed equipment, facilities, support staff and manpower; and

        - Renewal of the effectivity dates of the performance security after its expiration during the course of contract implementation.

      - Assignment and subcontracting of the contract or any part thereof or substitution of key personnel named in the proposal without prior written approval by the procuring entity.

      - Poor performance by the contractor or unsatisfactory quality and/or progress of work arising from his fault or negligence as reflected in the Constructor's Performance Evaluation System (“CPES”) rating sheet.  In the absence of the CPES rating sheet, the existing performance monitoring system of the procuring entity shall be applied.  Any of the following acts by the  Contractor shall be construed as poor performance:

        - Negative slippage of 15% and above within the critical path of the project due entirely to the fault or negligence of the contractor; and

        - Quality of materials and workmanship not complying with the approved specifications arising from the contractor's fault or negligence.

      - Willful or deliberate abandonment or non-performance of the project or contract by the contractor resulting to substantial breach thereof without lawful and/or just cause.

In addition to the penalty of suspension, the performance security posted by the contractor shall also be forfeited.

### Force Majeure, Release From Performance

For purposes of this Contract the terms “force majeure” and “fortuitous event” may be used interchangeably.  In this regard, a fortuitous event or force majeure shall be interpreted to mean an event which the Contractor could not have foreseen, or which though foreseen, was inevitable.  It shall not include ordinary unfavorable weather conditions; and any other cause the effects of which could have been avoided with the exercise of reasonable diligence by the Contractor.

If this Contract is discontinued by an outbreak of war or by any other event entirely outside the control of either the Procuring Entity or the Contractor, the Procuring Entity’s Representative shall certify that this Contract has been discontinued.  The Contractor shall make the Site safe and stop work as quickly as possible after receiving this certificate and shall be paid for all works carried out before receiving it and for any Work carried out afterwards to which a commitment was made.

If the event continues for a period of eighty four (84) days, either party may then give notice of termination, which shall take effect twenty eight (28) days after the giving of the notice.

After termination, the Contractor shall be entitled to payment of the unpaid balance of the value of the Works executed and of the materials and Plant reasonably delivered to the Site, adjusted by the following:

      - any sum to which the Contractor is entitled under GCC Clause 28;

      - the cost of his suspension and demobilization;

      - any sum to which the Procuring Entity is entitled.

The net balance due shall be paid or repaid within a reasonable time period from the time of the notice of termination.

### Resolution of Disputes

If any dispute or difference of any kind whatsoever shall arise between the parties in connection  with the implementation of the contract covered by the Act and this IRR, the parties shall make every effort to resolve amicably such dispute or difference by mutual consultation.

If the Contractor believes that a decision taken by the Procuring Entity’s Representative was either outside the authority given to the Procuring Entity’s Representative by this Contract or that the decision was wrongly taken, the decision shall be referred to the Arbiter indicated in the SCC within fourteen (14) days of the notification of the Procuring Entity’s Representative’s decision.

Any and all disputes arising from the implementation of this Contract covered by the R.A. 9184 and its IRR shall be submitted to arbitration in the Philippines according to the provisions of Republic Act No. 876, otherwise known as the “ Arbitration Law” and Republic Act 9285, otherwise known as the “Alternative Dispute Resolution Act of 2004”: Provided, however, That, disputes that are within the competence of the Construction Industry Arbitration Commission to resolve shall be referred thereto.  The process of arbitration shall be incorporated as a provision in this Contract that will be executed pursuant to the provisions of the Act and its IRR: Provided, further, That, by mutual agreement, the parties may agree in writing to resort to other alternative modes of dispute resolution.

### Suspension of Loan, Credit, Grant, or Appropriation

In the event that the Funding Source suspends the Loan, Credit, Grant, or Appropriation to the Procuring Entity, from which part of the payments to the Contractor are being made:

      - The Procuring Entity is obligated to notify the Contractor of such suspension within seven (7) days of having received the suspension notice.

      - If the Contractor has not received sums due it for work already done within forty five (45) days from the time the Contractor’s claim for payment has been certified by the Procuring Entity’s Representative, the Contractor may immediately issue a suspension of work notice in accordance with GCC Clause 45.2.

### Procuring Entity’s Representative’s Decisions

Except where otherwise specifically stated, the Procuring Entity’s Representative will decide contractual matters between the Procuring Entity and the Contractor in the role representing the Procuring Entity.

The Procuring Entity’s Representative may delegate any of his duties and responsibilities to other people, except to the Arbiter, after notifying the Contractor, and may cancel any delegation after notifying the Contractor.

### Approval of Drawings and Temporary Works by the Procuring Entity’s Representative

All Drawings prepared by the Contractor for the execution of the Temporary Works, are subject to prior approval by the Procuring Entity’s Representative before its use.

The Contractor shall be responsible for design of Temporary Works.

The Procuring Entity’s Representative’s approval shall not alter the Contractor’s responsibility for design of the Temporary Works.

The Contractor shall obtain approval of third parties to the design of the Temporary Works, when required by the Procuring Entity.

### Acceleration and Delays Ordered by the Procuring Entity’s Representative

When the Procuring Entity wants the Contractor to finish before the Intended Completion Date, the Procuring Entity’s Representative will obtain priced proposals for achieving the necessary acceleration from the Contractor.  If the Procuring Entity accepts these proposals, the Intended Completion Date will be adjusted accordingly and confirmed by both the Procuring Entity and the Contractor.

If the Contractor’s Financial Proposals for an acceleration are accepted by the Procuring Entity, they are incorporated in the Contract Price and treated as a Variation.

### Extension of the Intended Completion Date

The Procuring Entity’s Representative shall extend the Intended Completion Date if a Variation is issued which makes it impossible for the Intended Completion Date to be achieved by the Contractor without taking steps to accelerate the remaining work, which would cause the Contractor to incur additional costs.  No payment shall be made for any event which may warrant the extension of the Intended Completion Date.

The Procuring Entity’s Representative shall decide whether and by how much to extend the Intended Completion Date within twenty one (21) days of the Contractor asking the Procuring Entity’s Representative for a decision thereto after fully submitting all supporting information.  If the Contractor has failed to give early warning of a delay or has failed to cooperate in dealing with a delay, the delay by this failure shall not be considered in assessing the new Intended Completion Date.

### Right to Vary

The Procuring Entity’s Representative with the prior approval of the Procuring Entity may instruct Variations, up to a maximum cumulative amount of ten percent (10%) of the original contract cost.

Variations shall be valued as follows:

      - At a lump sum price agreed between the parties;

      - where appropriate, at rates in this Contract;

      - in the absence of appropriate rates, the rates in this Contract shall be used as the basis for valuation; or failing which

      - at appropriate new rates, equal to or lower than current industry rates and to be agreed upon by both parties and approved by the HoPE.

### Contractor's Right to Claim

If the Contractor incurs cost as a result of any of the events under GCC Clause 13, the Contractor shall be entitled to the amount of such cost. If as a result of any of the said events, it is necessary to change the Works, this shall be dealt with as a Variation.

### Dayworks

Subject to GCC Clause 43 on Variation Order, and if applicable as indicated in the SCC, the Dayworks rates in the Contractor’s bid shall be used for small additional amounts of work only when the Procuring Entity’s Representative has given written instructions in advance for additional work to be paid for in that way.

All work to be paid for as Dayworks shall be recorded by the Contractor on forms approved by the Procuring Entity’s Representative.  Each completed form shall be verified and signed by the Procuring Entity’s Representative within two days of the work being done.

The Contractor shall be paid for Dayworks subject to obtaining signed Dayworks forms.

### Early Warning

The Contractor shall warn the Procuring Entity’s Representative at the earliest opportunity of specific likely future events or circumstances that may adversely affect the quality of the work, increase the Contract Price, or delay the execution of the Works.  The Procuring Entity’s Representative may require the Contractor to provide an estimate of the expected effect of the future event or circumstance on the Contract Price and Completion Date.  The estimate shall be provided by the Contractor as soon as reasonably possible.

The Contractor shall cooperate with the Procuring Entity’s Representative in making and considering proposals for how the effect of such an event or circumstance can be avoided or reduced by anyone involved in the work and in carrying out any resulting instruction of the Procuring Entity’s Representative.

### Program of Work

Within the time stated in the SCC, the Contractor shall submit to the Procuring Entity’s Representative for approval a Program of Work showing the general methods, arrangements, order, and timing for all the activities in the Works.

An update of the Program of Work shall show the actual progress achieved on each activity and the effect of the progress achieved on the timing of the remaining work, including any changes to the sequence of the activities.

The Contractor shall submit to the Procuring Entity’s Representative for approval an updated Program of Work at intervals no longer than the period stated in the SCC.  If the Contractor does not submit an updated Program of Work within this period, the Procuring Entity’s Representative may withhold the amount stated in the SCC from the next payment certificate and continue to withhold this amount until the next payment after the date on which the overdue Program of Work has been submitted.

The Procuring Entity’s Representative’s approval of the Program of Work shall not alter the Contractor’s obligations.  The Contractor may revise the Program of Work and submit it to the Procuring Entity’s Representative again at any time.  A revised Program of Work shall show the effect of any approved Variations.

When the Program of Work is updated, the Contractor shall provide the Procuring Entity’s Representative with an updated cash flow forecast.  The cash flow forecast shall include different currencies, as defined in the Contract, converted as necessary using the Contract exchange rates.

All Variations shall be included in updated Program of Work produced by the Contractor.

### Management Conferences

Either the Procuring Entity’s Representative or the Contractor may require the other to attend a Management Conference.  The Management Conference shall review the plans for remaining work and deal with matters raised in accordance with the early warning procedure.

The Procuring Entity’s Representative shall record the business of Management Conferences and provide copies of the record to those attending the Conference and to the Procuring Entity.  The responsibility of the parties for actions to be taken shall be decided by the Procuring Entity’s Representative either at the Management Conference or after the Management Conference and stated in writing to all who attended the Conference.

### Bill of Quantities

The Bill of Quantities shall contain items of work for the construction, installation, testing, and commissioning of work to be done by the Contractor.

The Bill of Quantities is used to calculate the Contract Price.  The Contractor is paid for the quantity of the work done at the rate in the Bill of Quantities for each item.

If the final quantity of any work done differs from the quantity in the Bill of Quantities for the particular item and is not more than twenty five percent (25%) of the original quantity, provided the aggregate changes for all items do not exceed ten percent (10%) of the Contract price, the Procuring Entity’s Representative shall make the necessary adjustments to allow for the changes subject to applicable laws, rules, and regulations.

If requested by the Procuring Entity’s Representative, the Contractor shall provide the Procuring Entity’s Representative with a detailed cost breakdown of any rate in the Bill of Quantities.

### Instructions, Inspections and Audits

The Procuring Entity’s personnel shall at all reasonable times during construction of the Work be entitled to examine, inspect, measure and test the materials and workmanship, and to check the progress of the construction.

If the Procuring Entity’s Representative instructs the Contractor to carry out a test not specified in the Specification to check whether any work has a defect and the test shows that it does, the Contractor shall pay for the test and any samples.  If there is no defect, the test shall be a Compensation Event.

The Contractor shall permit the Funding Source named in the SCC to inspect the Contractor’s accounts and records relating to the performance of the Contractor and to have them audited by auditors appointed by the Funding Source, if so required by the Funding Source.

### Identifying Defects

The Procuring Entity’s Representative shall check the Contractor’s work and notify the Contractor of any defects that are found.  Such checking shall not affect the Contractor’s responsibilities.  The Procuring Entity’s Representative may instruct the Contractor to search uncover defects and test any work that the Procuring Entity’s Representative considers below standards and defective.

### Cost of Repairs

Loss or damage to the Works or Materials to be incorporated in the Works between the Start Date and the end of the Defects Liability Periods shall be remedied by the Contractor at the Contractor’s cost if the loss or damage arises from the Contractor’s acts or omissions.

### Correction of Defects

The Procuring Entity’s Representative shall give notice to the Contractor of any defects before the end of the Defects Liability Period, which is One (1) year from project completion up to final acceptance by the Procuring Entity’s Representative.

Every time notice of a defect is given, the Contractor shall correct the notified defect within the length of time specified in the Procuring Entity’s Representative’s notice.

The Contractor shall correct the defects which he notices himself before the end of the Defects Liability Period.

The Procuring Entity shall certify that all defects have been corrected. If the Procuring Entity considers that correction of a defect is not essential, he can request the Contractor to submit a quotation for the corresponding reduction in the Contract Price. If the Procuring Entity accepts the quotation, the corresponding change in the SCC is a Variation.

### Uncorrected Defects

The Procuring Entity shall give the Contractor at least fourteen (14) days notice of his intention to use a third party to correct a Defect. If the Contractor does not correct the Defect himself within the period, the Procuring Entity may have the Defect corrected by the third party. The cost of the correction will be deducted from the Contract Price.

The use of a third party to correct defects that are uncorrected by the Contractor will in no way relieve the Contractor of its liabilities and warranties under the Contract.

### Advance Payment

The Procuring Entity shall, upon a written request of the contractor which shall be submitted as a contract document, make an advance payment to the contractor in an amount not exceeding fifteen percent (15%) of the total contract price, to be made in lump sum or, at the most two, installments according to a schedule specified in the SCC.

The advance payment shall be made only upon the submission to and acceptance by the Procuring Entity of an irrevocable standby letter of credit of equivalent value from a commercial bank, a bank guarantee or a surety bond callable upon demand, issued by a surety or insurance company duly licensed by the Insurance Commission and confirmed by the Procuring Entity.

The advance payment shall be repaid by the Contractor by an amount equal to the percentage of the total contract price used for the advance payment.

The contractor may reduce his standby letter of credit or guarantee instrument by the amounts refunded by the Monthly Certificates in the advance payment.

The Procuring Entity will provide an Advance Payment on the Contract Price as stipulated in the Conditions of Contract, subject to the maximum amount stated in SCC Clause 39.1.

### Progress Payments

The Contractor may submit a request for payment for Work accomplished.  Such request for payment shall be verified and certified by the Procuring Entity’s Representative/Project Engineer.  Except as otherwise stipulated in the SCC, materials and equipment delivered on the site but not completely put in place shall not be included for payment.

The Procuring Entity shall deduct the following from the certified gross amounts to be paid to the contractor as progress payment:

      - Cumulative value of the work previously certified and paid for.

      - Portion of the advance payment to be recouped for the month.

      - Retention money in accordance with the condition of contract.

      - Amount to cover third party liabilities.

      - Amount to cover uncorrected discovered defects in the works.

Payments shall be adjusted by deducting therefrom the amounts for advance payments and retention.  The Procuring Entity shall pay the Contractor the amounts certified by the Procuring Entity’s Representative within twenty eight (28) days from the date each certificate was issued.  No payment of interest for delayed payments and adjustments shall be made by the Procuring Entity.

The first progress payment may be paid by the Procuring Entity to the Contractor provided that at least twenty percent (20%) of the work has been accomplished as certified by the Procuring Entity’s Representative.

Items of the Works for which a price of “0” (zero) has been entered will not be paid for by the Procuring Entity and shall be deemed covered by other rates and prices in the Contract.

### Payment Certificates

The Contractor shall submit to the Procuring Entity’s Representative monthly statements of the estimated value of the work executed less the cumulative amount certified previously.

The Procuring Entity’s Representative shall check the Contractor’s monthly statement and certify the amount to be paid to the Contractor.

The value of Work executed shall:

      - be determined by the Procuring Entity’s Representative;

      - comprise the value of the quantities of the items in the Bill of Quantities completed; and

      - include the valuations of approved variations.

The Procuring Entity’s Representative may exclude any item certified in a previous certificate or reduce the proportion of any item previously certified in any certificate in the light of later information.

### Retention

The Procuring Entity shall retain from each payment due to the Contractor an amount equal to a percentage thereof using the rate as specified in GCC Sub-Clause 42.2.

Progress payments are subject to retention of ten percent (10%), referred to as the “retention money.”  Such retention shall be based on the total amount due to the Contractor prior to any deduction and shall be retained from every progress payment until fifty percent (50%) of the value of Works, as determined by the Procuring Entity, are completed.  If, after fifty percent (50%) completion, the Work is satisfactorily done and on schedule, no additional retention shall be made; otherwise, the ten percent (10%) retention shall again be imposed using the rate specified therefor.

The total “retention money” shall be due for release upon final acceptance of the Works.  The Contractor may, however, request the substitution of the retention money for each progress billing with irrevocable standby letters of credit from a commercial bank, bank guarantees or surety bonds callable on demand, of amounts equivalent to the retention money substituted for and acceptable to the Procuring Entity, provided that the project is on schedule and is satisfactorily undertaken.  Otherwise, the ten (10%) percent retention shall be made.  Said irrevocable standby letters of credit, bank guarantees and/or surety bonds, to be posted in favor of the Government shall be valid for a duration to be determined by the concerned implementing office/agency or Procuring Entity and will answer for the purpose for which the ten (10%) percent retention is intended, i.e., to cover uncorrected discovered defects and third party liabilities.

On completion of the whole Works, the Contractor may substitute retention money with an “on demand” Bank guarantee in a form acceptable to the Procuring Entity.

### Variation Orders

Variation Orders may be issued by the Procuring Entity to cover any increase/decrease in quantities, including the introduction of new work items that are not included in the original contract or reclassification of work items that are either due to change of plans, design or alignment to suit actual field conditions resulting in disparity between the preconstruction plans used for purposes of bidding and the “as staked plans” or construction drawings prepared after a joint survey by the Contractor and the Procuring Entity after award of the contract, provided that the cumulative amount of the Variation Order does not exceed ten percent (10%) of the original project cost. The addition/deletion of Works should be within the general scope of the project as bid and awarded. The scope of works shall not be reduced so as to accommodate a positive Variation Order. A Variation Order may either be in the form of a Change Order or Extra Work Order.

A Change Order may be issued by the Procuring Entity to cover any increase/decrease in quantities of original Work items in the contract.

An Extra Work Order may be issued by the Procuring Entity to cover the introduction of new work necessary for the completion, improvement or protection of the project which were not included as items of Work in the original contract, such as, where there are subsurface or latent physical conditions at the site differing materially from those indicated in the contract, or where there are duly unknown physical conditions at the site of an unusual nature differing materially from those ordinarily encountered and generally recognized as inherent in the Work or character provided for in the contract.

Any cumulative Variation Order beyond ten percent (10%) shall be subject of another contract to be bid out if the works are separable from the original contract.  In exceptional cases where it is urgently necessary to complete the original scope of work, the HoPE may authorize a positive Variation Order go beyond ten percent (10%) but not more than twenty percent (20%) of the original contract price, subject to the guidelines to be determined by the GPPB: Provided, however, That appropriate sanctions shall be imposed on the designer, consultant or official responsible for the original detailed engineering design which failed to consider the Variation Order beyond ten percent (10%).

In claiming for any Variation Order, the Contractor shall, within seven (7) calendar days after such work has been commenced or after the circumstances leading to such condition(s) leading to the extra cost, and within twenty-eight (28) calendar days deliver a written communication giving full and detailed particulars of any extra cost in order that it may be investigated at that time. Failure to provide either of such notices in the time stipulated shall constitute a waiver by the contractor for any claim. The preparation and submission of Variation Orders are as follows:

      - If the Procuring Entity’s representative/Project Engineer believes that a Change Order or Extra Work Order should be issued, he shall prepare the proposed Order accompanied with the notices submitted by the Contractor, the plans therefore, his computations as to the quantities of the additional works involved per item indicating the specific stations where such works are needed, the date of his inspections and investigations thereon, and the log book thereof, and a detailed estimate of the unit cost of such items of work, together with his justifications for the need of such Change Order or Extra Work Order, and shall submit the same to the HoPE for approval.

      - The HoPE or his duly authorized representative, upon receipt of the proposed Change Order or Extra Work Order shall immediately instruct the appropriate technical staff or office of the Procuring Entity to conduct an on-the-spot investigation to verify the need for the Work to be prosecuted and to review the proposed plan, and prices of the work involved.

      - The technical staff or appropriate office of the Procuring Entity shall submit a report of their findings and recommendations, together with the supporting documents, to the Head of Procuring Entity or his duly authorized representative for consideration.

      - The HoPE or his duly authorized representative, acting upon the recommendation of the technical staff or appropriate office, shall approve the Change Order or Extra Work Order after being satisfied that the same is justified, necessary, and in order.

      - The timeframe for the processing of Variation Orders from the preparation up to the approval by the Procuring Entity concerned shall not exceed thirty (30) calendar days.

### Contract Completion

Once the project reaches an accomplishment of ninety five (95%) of the total contract amount, the Procuring Entity may create an inspectorate team to make preliminary inspection and submit a punch-list to the Contractor in preparation for the final turnover of the project. Said punch-list will contain, among others, the remaining Works, Work deficiencies for necessary corrections, and the specific duration/time to fully complete the project considering the approved remaining contract time. This, however, shall not preclude the claim of the Procuring Entity for liquidated damages.

### Suspension of Work

The Procuring Entity shall have the authority to suspend the work wholly or partly by written order for such period as may be deemed necessary, due to force majeure or any fortuitous events or for failure on the part of the Contractor to correct bad conditions which are unsafe for workers or for the general public, to carry out valid orders given by the Procuring Entity or to perform any provisions of the contract, or due to adjustment of plans to suit field conditions as found necessary during construction. The Contractor shall immediately comply with such order to suspend the work wholly or partly.

The Contractor or its duly authorized representative shall have the right to suspend work operation on any or all projects/activities along the critical path of activities after fifteen (15) calendar days from date of receipt of written notice from the Contractor to the district engineer/regional director/consultant or equivalent official, as the case may be, due to the following:

      - There exist right-of-way problems which prohibit the Contractor from performing work in accordance with the approved construction schedule.

      - Requisite construction plans which must be owner-furnished are not issued to the contractor precluding any work called for by such plans.

      - Peace and order conditions make it extremely dangerous, if not possible, to work. However, this condition must be certified in writing by the Philippine National Police (PNP) station which has responsibility over the affected area and confirmed by the Department of Interior and Local Government (DILG) Regional Director.

      - There is failure on the part of the Procuring Entity to deliver government-furnished materials and equipment as stipulated in the contract.

      - Delay in the payment of Contractor’s claim for progress billing beyond forty-five (45) calendar days from the time the Contractor’s claim has been certified to by the procuring entity’s authorized representative that the documents are complete unless there are justifiable reasons thereof which shall be communicated in writing to the Contractor.

In case of total suspension, or suspension of activities along the critical path, which is not due to any fault of the Contractor, the elapsed time between the effectivity of the order suspending operation and the order to resume work shall be allowed the Contractor by adjusting the contract time accordingly.

### Payment on Termination

If the Contract is terminated because of a fundamental breach of Contract by the Contractor, the Procuring Entity’s Representative shall issue a certificate for the value of the work done and Materials ordered less advance payments received up to the date of the issue of the certificate and less the percentage to apply to the value of the work not completed, as indicated in the SCC. Additional Liquidated Damages shall not apply.  If the total amount due to the Procuring Entity exceeds any payment due to the Contractor, the difference shall be a debt payable to the Procuring Entity.

If the Contract is terminated for the Procuring Entity’s convenience or because of a fundamental breach of Contract by the Procuring Entity, the Procuring Entity’s Representative shall issue a certificate for the value of the work done, Materials ordered, the reasonable cost of removal of Equipment, repatriation of the Contractor’s personnel employed solely on the Works, and the Contractor’s costs of protecting and securing the Works, and less advance payments received up to the date of the certificate.

The net balance due shall be paid or repaid within twenty eight (28) days from the notice of termination.

If the Contractor has terminated the Contract under GCC Clauses 17 or 18, the Procuring Entity shall promptly return the Performance Security to the Contractor.

### Extension of Contract Time

Should the amount of additional work of any kind or other special circumstances of any kind whatsoever occur such as to fairly entitle the contractor to an extension of contract time, the Procuring Entity shall determine the amount of such extension; provided that the Procuring Entity is not bound to take into account any claim for an extension of time unless the Contractor has, prior to the expiration of the contract time and within thirty (30) calendar days after such work has been commenced or after the circumstances leading to such claim have arisen, delivered to the Procuring Entity notices in order that it could have investigated them at that time. Failure to provide such notice shall constitute a waiver by the Contractor of any claim. Upon receipt of full and detailed particulars, the Procuring Entity shall examine the facts and extent of the delay and shall extend the contract time completing the contract work when, in the Procuring Entity’s opinion, the findings of facts justify an extension.

No extension of contract time shall be granted the Contractor due to (a) ordinary unfavorable weather conditions and (b) inexcusable failure or negligence of Contractor to provide the required equipment, supplies or materials.

Extension of contract time may be granted only when the affected activities fall within the critical path of the PERT/CPM network.

No extension of contract time shall be granted when the reason given to support the request for extension was already considered in the determination of the original contract time during the conduct of detailed engineering and in the preparation of the contract documents as agreed upon by the parties before contract perfection.

Extension of contract time shall be granted for rainy/unworkable days considered unfavorable for the prosecution of the works at the site, based on the actual conditions obtained at the site, in excess of the number of rainy/unworkable days pre-determined by the Procuring Entity in relation to the original contract time during the conduct of detailed engineering and in the preparation of the contract documents as agreed upon by the parties before contract perfection, and/or for equivalent period of delay due to major calamities such as exceptionally destructive typhoons, floods and earthquakes, and epidemics, and for causes such as non-delivery on time of materials, working drawings, or written information to be furnished by the Procuring Entity, non-acquisition of permit to enter private properties or non-execution of deed of sale or donation within the right-of-way resulting in complete paralyzation of construction activities, and other meritorious causes as determined by the Procuring Entity’s Representative and approved by the HoPE. Shortage of construction materials, general labor strikes, and peace and order problems that disrupt construction operations through no fault of the Contractor may be considered as additional grounds for extension of contract time provided they are publicly felt and certified by appropriate government agencies such as DTI, DOLE, DILG, and DND, among others. The written consent of bondsmen must be attached to any request of the Contractor for extension of contract time and submitted to the Procuring Entity for consideration and the validity of the Performance Security shall be correspondingly extended.

### Price Adjustment

Except for extraordinary circumstances as determined by NEDA and approved by the GPPB, no price escalation shall be allowed.  Nevertheless,  in cases where the cost of the awarded contract is affected by any applicable new laws, ordinances, regulations, or other acts of the GoP, promulgated after the date of bid opening, a contract price adjustment shall be made or appropriate relief shall be applied on a no loss-no gain basis.

### Completion

The Contractor shall request the Procuring Entity’s Representative to issue a certificate of Completion of the Works, and the Procuring Entity’s Representative will do so upon deciding that the work is completed.

### Taking Over

The Procuring Entity shall take over the Site and the Works within seven (7) days from the date the Procuring Entity’s Representative issues a certificate of Completion.

### Operating and Maintenance Manuals

If “as built” Drawings and/or operating and maintenance manuals are required, the Contractor shall supply them by the dates stated in the SCC.

If the Contractor does not supply the Drawings and/or manuals by the dates stated in the SCC, or they do not receive the Procuring Entity’s Representative’s approval, the Procuring Entity’s Representative shall withhold the amount stated in the SCC from payments due to the Contractor.

# Section V. Special Conditions of Contract

Notes on the Special Conditions of Contract Similar to the Section III. Bid Data Sheet, the clauses in this Section are intended to assist the Procuring Entity in providing contract-specific information in relation to corresponding clauses in the GCC. The provisions of this Section complement the GCC, specifying contractual requirements linked to the special circumstances of the Procuring Entity, the Procuring Entity’s country, the sector, and the Works procured. In preparing this Section, the following aspects should be checked: Information that complements provisions of Section IV. General Conditions of Contract must be incorporated. Amendments and/or supplements to provisions of Section IV. General Conditions of Contract, as necessitated by the circumstances of the specific project, must also be incorporated. However, no special condition which defeats or negates the general intent and purpose of the provisions of Section IV. General Conditions of Contract should be incorporated herein. For foreign-assisted projects, the Special Conditions of Contract to be used is provided in Section X-Foreign-Assisted Projects.

Special Conditions of Contract

| GCC Clause |  |
| --- | --- |
| 1.17 | The Intended Completion Date is 210 calendar days from the effective date of the contract. NOTE: The contract duration shall be reckoned from the start date and not from contract effectivity date. |
| 1.22 | The Procuring Entity is Philippine Ports Authority, PMO-Panay/Guimaras, Brgy. Loboc, La Paz, Iloilo City . |
| 1.23 | The Procuring Entity’s Representative is Mr. Jose Cesario O. Bautista, Port Manager. |
| 1.24 | The Site is located at Port of Estancia, Iloilo and is defined in drawings No. [as attached]. List here locations of other Sites, if any. |
| 1.28 | The Start Date is upon receipt of the Notice to Proceed. NOTE: The start date shall be the date of receipt of the Notice to Proceed. |
| 1.31 | The Works consist of : 1.00 Mobilization/Demobilization 2.00 Removal of Vinyl Floor Tiles 3.00 3.01 3.02 3.03 Installation of Floor Tiles Supply, Deliver and Install Floor Tiles (Ground Floor) Supply, Deliver and Install Floor Tiles ( 2nd Floor ) Supply, Deliver and Install Floor Tiles(Stair) 4.00 4.01 4.02 4.03 5.00 Demolition,Disposal of old wooden partition & Construction of new partitions Remove & dispose of old wooden partition to designated area directed by engineer. Fabrication of wooden Partition and installation of glass partition incdg.finishing Surface Preparation, Prime and Final Painting of Doors & Item 4.02. Repair of PTB Ceiling 5.01 Removal and dispose of existing ceiling incdg stockpiling to designated area. 5.02 Supply, Deliver and Install of Ceiling including joist and boards (Ground & 2nd Floor) 6.00 6.01 6.02 6.03 6.04 Remove, Dispose and Install Doors & Windows Remove & dispose of old doors & windows to designated site Supply/Deliver and Install new set of Doors(10sets) and Windows(27) Leveling / Finishing of Windows / Door Sill Painting of Doors 7.00 7.01 7.02 8.00 9.00 9.01 9.02 Repair of PTB Roofings Removal and Disposal of old Corr.G.I Sheets and other accessories Supply, Deliver and Install of new Roofing and accessories. Paintings of Concrete Walls (Interior & Exterior),Parapet wall, wooden Partitions trusses and misc.roofings accessories Electricals Fixtures and Receptacles Power Panels & Service Equipment |
| 2.2 | If different dates are specified for completion of the Works by section (“sectional completion”), these dates should be listed here |
| 5.1 | The Procuring Entity shall give possession of all parts of the Site to the Contractor [insert date]. |
| 6.5 | The Contractor shall employ the following Key Personnel: Project Manager, Project Engineer, Materials Engineer, Construction Safety and Health Officer, Foreman. NOTE: The names of the Key Personnel and their designation shall be filled out by winning contractor prior to contract signing. |
| 7.4(c) | Specify additional conditions, if any, that must be met prior to the release of the performance security; otherwise, state “No further instructions.” |
| 7.7 | No further instructions. |
| 8.1 | No further instructions. |
| 10 | The site investigation reports are: [list here or state none] |
| 12.3 | No further instructions. |
| 12.5 | Select one, delete the other. In case of permanent structures, such as buildings of types 4 and 5 as classified under the National Building Code of the Philippines and other structures made of steel, iron, or concrete which comply with relevant structural codes (e.g., DPWH Standard Specifications), such as, but not limited to, steel/concrete bridges, flyovers, aircraft movement areas, ports, dams, tunnels, filtration and treatment plants, sewerage systems, power plants, transmission and communication towers, railway system, and other similar permanent structures: Fifteen (15) years. In case of semi-permanent structures, such as buildings of types 1, 2, and 3 as classified under the National Building Code of the Philippines, concrete/asphalt roads, concrete river control, drainage, irrigation lined canals, river landing, deep wells, rock causeway, pedestrian overpass, and other similar semi-permanent structures: Five (5) years. In case of other structures, such as Bailey and wooden bridges, shallow wells, spring developments, and other similar structures: Two (2) years. |
| 13 | State here “No additional provision.” or, if the Contractor is a joint venture, “All partners to the joint venture shall be jointly and severally liable to the Procuring Entity.” |
| 18.3(h)(i) | No further instructions. |
| 21.2 | The Arbiter is: [Insert name] [Insert address] |
| 29.1 | Select one, delete the other: Day works are applicable at the rate shown in the Contractor’s original Bid. |
| 31.1 | The Contractor shall submit the Program of Work to the Procuring Entity’s Representative within [insert number] days of delivery of the Notice of Award. |
| 31.3 | The period between Program of Work updates is [insert number] days. The amount to be withheld for late submission of an updated Program of Work is [insert amount]. |
| 34.3 | The Funding Source is the Government of the Philippines. |
| 39.1 | The amount of the advance payment is 15% of the ABC. |
| 40.1 | Select one and delete the other. No further instructions. Or Materials and equipment delivered on the site but not completely put in place shall be included for payment. |
| 51.1 | The date by which operating and maintenance manuals are required is [date]. The date by which “as built” drawings are required is [date]. |
| 51.2 | The amount to be withheld for failing to produce “as built” drawings and/or operating and maintenance manuals by the date required is [amount in local currency]. |

# Section VI. Specifications

Notes on Specifications A set of precise and clear specifications is a prerequisite for Bidders to respond realistically and competitively to the requirements of the Procuring Entity without qualifying or conditioning their Bids. In the context of international competitive bidding, the specifications must be drafted to permit the widest possible competition and, at the same time, present a clear statement of the required standards of workmanship, materials, and performance of the goods and services to be procured. Only if this is done will the objectives of economy, efficiency, and fairness in procurement be realized, responsiveness of Bids be ensured, and the subsequent task of bid evaluation facilitated. The specifications should require that all goods and materials to be incorporated in the Works be new, unused, of the most recent or current models, and incorporate all recent improvements in design and materials unless provided otherwise in the Contract. Samples of specifications from previous similar projects are useful in this respect. The use of metric units is mandatory. Most specifications are normally written specially by the Procuring Entity or its representative to suit the Works at hand. There is no standard set of Specifications for universal application in all sectors in all regions, but there are established principles and practices, which are reflected in these PBDs. There are considerable advantages in standardizing General Specifications for repetitive Works in recognized public sectors, such as highways, ports, railways, urban housing, irrigation, and water supply, in the same country or region where similar conditions prevail. The General Specifications should cover all classes of workmanship, materials, and equipment commonly involved in construction, although not necessarily to be used in a particular Works Contract. Deletions or addenda should then adapt the General Specifications to the particular Works. Care must be taken in drafting specifications to ensure that they are not restrictive. In the specification of standards for goods, materials, and workmanship, recognized international standards should be used as much as possible. Where other particular standards are used, whether national standards or other standards, the specifications should state that goods, materials, and workmanship that meet other authoritative standards, and which ensure substantially equal or higher quality than the standards mentioned, will also be acceptable. The following clause may be inserted in the SCC. Sample Clause: Equivalency of Standards and Codes Wherever reference is made in the Contract to specific standards and codes to be met by the goods and materials to be furnished, and work performed or tested, the provisions of the latest current edition or revision of the relevant standards and codes in effect shall apply, unless otherwise expressly stated in the Contract. Where such standards and codes are national, or relate to a particular country or region, other authoritative standards that ensure a substantially equal or higher quality than the standards and codes specified will be accepted subject to the Procuring Entity’s Representative’s prior review and written consent. Differences between the standards specified and the proposed alternative standards shall be fully described in writing by the Contractor and submitted to the Procuring Entity’s Representative at least twenty eight (28) days prior to the date when the Contractor desires the Procuring Entity’s Representative’s consent. In the event the Procuring Entity’s Representative determines that such proposed deviations do not ensure substantially equal or higher quality, the Contractor shall comply with the standards specified in the documents. These notes are intended only as information for the PRO Procuring Entity or the person drafting the Bidding Documents. They should not be included in the final Bidding Documents.

GENERAL SCOPE OF WORK

The scope of work shall include the furnishing and installation of all items of construction materials, equipment and labor necessary for the project.

MOBILIZATION AND DEMOBILIZATION

SCOPE

This Chapter of the Specifications refers to the Mobilization and Demobilization.  It includes the supply at the Site of all plant and equipment required for the execution of the works, together with everything necessary to maintain the said equipment and plant and performance of the maintenance during the construction period.  On completion of the works all plant, equipment and materials shall be removed including clean up of the premises.

# MOBILIZATION

## PLANT EQUIPMENT

Mobilization includes the following:

- Assembly, preparation and loading for shipment of all plant and equipment at the contractor’s home station or source of supply.

- Transportation of plant, equipment and material from the home station or source of supply to the site.

- Unload and install, ready for use, all plant and equipment and whatever else required for the execution of the works.

- Maintain the plant and equipment during the construction.

- Install all telephone and communication systems, electricity and water supply lines, including their meters; construct all temporary roads, temporary port fence and gate and sanitary facilities necessary and gate for the execution of works.

- Install fixed points for the setting out of the structures.

- Provide and maintain during the construction period land and sea transportation equipment including crew, where and when necessary, for the use of the Engineer on Site.

- Provide the erect to the approval of the Engineer such supports as may be required to protect efficiently all structures or work which may be endangered by the execution of the works and he shall remove such supports on completion of the works or otherwise task such permanent measures as may be required by the Engineer to protect the structures of works.

Other matters

Mobilization shall also include the following:

- The cost of insurance as required in the contract.

- Payments of sundry expenses, such as all fees and permits, for water, electricity, telephone, cleaning of offices and vehicles.

### DEMOBILIZATION

Demobilization shall include the following:

- The dismantling, preparation and loading for removal and shipment of all contractors’ plant, installation and equipment at the site.

- The transportation of all the above plant, equipment and materials from the Site to the home station or somewhere else outside the site.

- Dismantling and removing of all temporary building and structures.

- The clean up of the Site and Work Area in a satisfactory manner and removal of material, debris, waste, etc. from the Port Area, and make good damage or temporary alternations to the temporary building or installations.

## ADDITIONAL ITEMS AND CONDITIONS

The description above are stated in brief; the Contractor must study all Contract Documents and have to include in his itemized unit prices allowances for any work and services not specially itemized above or in any other pay items in the Specifications and Bills of Quantities.

DEMOLITION AND REMOVAL

SCOPE

The work includes the furnishing of all labor, materials & equipment require to carry out the demolition and removal of obstruction, portions of existing pier including extraction/cutting of timber of RC piles at required depth and demolition of miscellaneous buildings, pavements, fences, utilities, navigation aides and wrecks & etc., required for the execution of contract.

The contractor shall submit to the proposed methodology & procedure of demolition work with detail drawings and calculations if necessary, to the Engineer for approval, before the execution of the Works.

The contractors shall keep of pavements and landing areas to and from to the site of the disposal area clean and free of mud, dirt & debris during and after the execution of disposal. Disposal of debris and materials shall be as directed by the Engineer.

For offshore obstructions to pile driving & dredging, survey shall be executed by the Contractor with the Engineer before any demolition & removal of wrecks is commence and shall be as directed by the Engineer.

## OWNERSHIP OF DEMOLISHED  MATERIAL

Materials coming from the demolition works except general earth shall remain the property of the Employer and shall be stored properly by the Contractor at a place designated by the Engineer.

## INTEREFERENCE WITH PORT OPERATIONS

During the execution of the work, the Contractor shall not interfere with shipping, navigation and other traffic in the work, the Contractor shall not interfere with the shipping, navigation and other traffic in the port.

The Contractor shall make arrangements with the operations people on the schedule of demolition and related works to keep port operation activities undisturbed at all times.

Prior to commencement of the demolition works, the Contractor shall inform/announce to port users the schedule of disconnection of utilities.

## EXECUTION

- Prior to the commencement of demolition works, the alignments of the new construction works to existing pier shall be checked.

- The width and alignment of the existing structure to be demolished shall be marked by paint.

- With these lines as guides, concrete shall be broken and reinforcing bars cut, such that panels or portions of the structure can be lifted out for disposal outside of the operational work area.

- Extract concrete piles with care in order not to damage existing or adjacent structures, equipment or materials.

- Extract timber fender piles with care so as to remove all timber to finish dredge level extraction or by cutting as shown in the drawings.

- Remove rocks from existing slope protection and store for re-use in new construction.

- Demolished buildings, pavements, curbs, fences, utilities, services, navigation aids and the like as determined in the field for each project and as shown on the drawings or as directed by the Engineer.

## SAFETY

During the course of survey and clearing, any obstacles which are recognized and seemed to be explosive or hazardous to workers shall be removed from the site by the Employer.

At the end of each day’s work, the Contractor shall keep the workplace in safe condition, so that no part is in danger of falling or creating hazard to personnel or equipment.

## REINFORCED CONCRETE

## General

All works falling under this category shall include reinforced concrete for all kinds and parts of any reinforced concrete structure.

## Materials

## Cement

Cement used shall be Type I Portland Cement conforming to the requirements of the latest revision of ASTM C 150 “Standard Specifications for Portland Cement”.

## Coarse Aggregates

Coarse aggregates shall be washed, well graded, hard pieces of gravel, or rock conforming to the requirements of ASTM C 33 “Standard Specifications for Concrete Aggregates”.

## Fine Aggregates

Fine aggregates shall be washed sand, stone screenings or other inert materials of same characteristics, or any combination thereof composed of clean, hard, strong uncoated grains and free from injurious amounts of dust, lumps of clay, shale, alkali, and organic matter. It shall conform to the requirements of ASTM C 33 “Standard Specifications for Concrete Aggregates”. Beach sand shall not be used unless approved by the Engineer.

## Admixture

Unless otherwise required by field conditions, admixture maybe used subject to the expressed approval of the engineer. The cost thereof shall be considered as already included in the unit cost bid of the contractor for the concrete.

## Storage of Materials

- Cement shall be stockpiled as closely as possible in water proof storage sheds, stacks suitably elevated above ground to prevent cement absorption of moisture.

- Aggregates shall be placed in stockpile in a manner preventing segregation thereof and contamination with foreign materials.

- Reinforcing steel bars shall be stored properly covered and protected from humidity to prevent rusting and/or coating with oil, dirt or other objectionable matters.

## Designed Strengths of Concrete

Concrete for structural parts or members shall develop a minimum 28-day compressive cylinder strength of 4,000 psi, unless otherwise indicated in the drawing and non-structural parts or members such as partition walls and slab on fill shall develop a minimum 28-day strength of 2,500 psi, unless otherwise specified in the drawings.

## Trial Batch for Concrete

Thirty (30) calendar days before the start of concreting works, the contractor shall submit design mixes and the corresponding test results made on sample thereof. Sampling and testing shall be in accordance with the ASTM Standard procedures for sampling and testing, for the particular design strength(s) required.

The particulars of the mix such as the slump and the proportionate weights of cement, saturated surface dry aggregates and water used shall be stated. Test results shall show 28-day strength(s) fifteen (15) percent higher than the ultimate strength(s) required.

## Concrete Proportion and Consistency

Concrete proportions should produce mix consistencies that will work readily into angles and corners of the forms and around reinforcements irrespective of the method of placing employed, without permitting the materials to segregate or excess water to collect on the surface of the concrete and with separated individual particles of aggregates showing coating of mortar with proportionate amount of sand. The total aggregate in the proportion used shall be such that when sieved, the weight passing the No.4 standard Sieve shall be thirty percent (30%) of the total.

The methods used for measuring materials going into the concrete mix shall permit easy checking and control of proportions at any time during the work.

## Mixing of Concrete

All concrete used shall be machine-mixed at the site. Each batch shall be mixed at the mixer’s design speed, for at least 1½ minute after all concrete materials are simultaneously placed in the mixer. The ideal rotation speed of the mixer shall between 14 and 20 rpm.

All mix contents of the mixer shall be thoroughly removed before any succeeding batch is placed.

The materials for the first batch shall contain sufficiently excess cement, sand and water to coat the inside walls of the mixer without reducing the required mortar content of the mix.

The mixer shall provide with devices for accurately measuring and controlling the amount of water used in each batch and for automatically recording the number of revolutions of the mixer.

Hand mixing of concrete will only be allowed in case of mixer breakdown, in which case it shall stopped as soon as pouring for particular section is completed, or at a construction joint as directed by the Engineer.

Re-tempering or remixing of partially hardened concrete with the addition of water will not be permitted.

## Placing of Concrete

- Concrete shall be placed in the presence of the Engineer only after the forms, reinforcing bars and other spaces to receive the concrete have been inspected and approved by the engineer.

- Concrete shall be placed only when wind and weather conditions will allow proper placement and curing of the concrete. Notice of any concreting operations shall serve to the Engineer at least three (3) days ahead of each schedule.

- Mixed concrete shall be deposited in its final position within a practicable time. Each succeeding fresh deposit for particular structural member shall be placed at a practicable rate to prevent cold joints. Each successive fresh deposit of concrete shall be vibrated vertically at uniformly spaced points and levels, of such duration and intensity to compact the concrete thoroughly but shall be continued the moment segregation of materials is noticed.

- Where concreting operations involve a  fall more than 1.5  meters (4.92 feet), the fresh concrete shall be poured through approved sheet metal conduit pipes. The pipes shall be kept full of concrete and its lower end kept below the surface of concrete throughout the pouring operations.

- Deposition of concrete shall be in such a way as to prevent segregation of the materials and the displacement of the reinforcement. Placing shall be done preferably with the use of buggies, buckets or wheel-borrows. Troughs, conveyors and pipes and the manner of use of each one shall be with the expressed permission of the Engineer.

- Each layer of concrete shall be placed approximately normal as possible in uniform layers not exceeding 0.30meters, unless otherwise ordered. The rate of placing concrete in the forms shall preferably be 0.025 meters (0.082 ft) vertical rise per minute.

## Construction Joints

During stoppage of concrete pouring operations, when jointing of old concrete becomes necessary, the following point should be observed:

- Construction joint not indicated in the drawing shell be located as to least affect the strength of the structure. Such locations will be as pointed out by the Engineer.

## Forms and Falsework

All forms and falsework to be used in the work must be designated, and constructed by the contractor for rigidity and adequacy for carrying the loads of the fresh concrete and/or additional superimposed construction loads. The Authority may form time to time verify the adequacy and safety of such temporary works and may require the contractor to submit detailed design drawings of forms and falseworks proposed to be used. Approval of such drawings or design of forms, however, shall not relieve the contractor of his liability on resulting imperfections or damages to the finished concrete, or other damages which may directly result there from.

Forms may be re-used but shall be scraped by a wire brush of all clinging mortar. Bulges should be planed and realigned prior to its use.

Prior to placing concrete form surfaces should be oiled for easy form removal. However, the oil coating should not be so thick as to stain and soften the concrete surface. Oil coatings should be applied before rebars are placed.

## Curing and Waterproofing

All concrete shall be cured for at least 14 days after the date of placing in accordance with approved and accepted methods.

## Finishing of Concrete Surfaces

Concrete surfaces shall conform accurately to the form, alignment, grades and sections shown on drawings or as prescribed by the Engineer. It shall be free from bulges, ridges, honeycombing or roughness of any kind, and shall be of a reasonably smooth wood float finish.

## Treatment of Surface Defects

All irregular concrete surfaces, voids, holes, honeycombs exposed after the contractor in such a way shall repair removal that the repaired surface would acceptable under paragraph on finishing of concrete surfaces above.

## Architectural Finish

All exposed concrete exterior surfaces shall be given an architectural finish as directed by the Engineer.

## Placing Reinforcement

Metal reinforcement shall be placed as accurately detailed on drawings and properly secured by approved means.

All bars shall be cold bent unless approved otherwise by the Engineer. Minimum distance between parallel bars shall be one and one-half (1 ½) times the diameter for round bars and twice the side dimension for square bars. The clear distance between bars shall not be less than 2.54 cm (1 inch) nor less that one and one-third (1 1/3) times the maximum size of the course aggregate, whichever is bigger.

All reinforcing steel shall be cleaned of all rust or scale and deleterious which tend to destroy the bond between the concrete and the steel.

## Reinforcing Bar Splices

Generally, splice/s of reinforcement at points of maximum stress especially in slabs, beams and girders shall be avoided. Such splice/s may however be approved by the Engineer in writing provided the lap if bonded or butt welded is sufficient to transfer tensile stress between bars by at least 125% of the specified yield strength of the reinforcing bar. For adjacent bars splices shall be staggered.

## Ready Mix Concrete

Where ready-mix concrete is used the requirements specified for batching, mixing and transporting shall be in accordance with the requirements set forth in ASTM C 94 “Specifications for Ready-Mix Concrete” unless otherwise specified.

The contractor shall notify the Engineer seven (7) days in advance before any continuous phase of concreting operations is started. Upon notification, the General Manager shall have the right to inspect the ready-mix concrete supplier’s plant/equipment and all materials and/or sources thereof. The contractor must coordinate with the supplier and must provide safe and adequate guidance for the General Manager or his representative in conducting such examinations.

For all ready-mixed concrete delivered to the site of work, discharge shall be completed within one-hour after the addition of cement to the aggregates or before the drum is revolved 25 times, whichever comes first. Under conditions contributing to the stiffening of concrete especially during hot weather the time required between the introduction of cement to the aggregates and discharge of the mix may still be reduced by the Engineer.

Truck mixers shall be equipped with counters indicating the number of revolutions of the drums, which shall be automatically actuated at the time of starting mixers at mixing speeds.

Each batch or truck delivery of concrete shall be mixed inside the drum for not less than 70 revolutions of the drum at the rate of rotation designated by the equipment manufacturer. Additional mixing if ordered by the Engineer shall be at the speed designated as agitating speed by the manufacturer of the equipment.

Concrete for individual batches or deliveries should be of uniform consistency, mix and grading. If slump tests of a minimum 2 samples taken within 15 minutes of each other at approximately 15% and 85% discharge load give values differing more than 2.54 cm (1 inch) when the specified slump is 76 mm (3 inches) or less, or if the difference is more than 50 mm (2 inches) when specified slump is more than 76 mm (3 inches), use of the particular mixer in the work shall be stopped until corrections are made to prevent such conditions, which shall be confirmed by further slump tests.

Every batch of ready-mixed concrete delivered at the jobsite shall be accompanied by a ticket furnished in accordance with Section 15 of ASTM C94. The time when the materials were batched shall also be indicated.

Non-agitating equipment or combination truck and trailer equipment for transporting concrete will not be permitted.

The authority reserves the right to verify from time to time the quality and quantity of materials used in every cement batch from the batching plant. The Contractor shall be aware of this provision and make the proper arrangement with the concrete supplier.

## Test on Concrete

Test on concrete shall be in accordance with the following:

Concrete Samples for tests shall be secured and molded in accordance with ASTM C172 – “Method of Sampling Concrete”, and ASTM C 31 – “Method of Making and Curing, Concrete Compression and Flexure Test Specimens in Field”.

Strength Tests on samples shall be made in accordance with ASTM C 39 – “Standard Method of Test for Compressive Strength of Molded Concrete Cylinder”.

Not less than four (4) cylindrical specimens shall be made for each test of which at least two (2) shall be reserved for 28-day test. Not less than one (1) test shall be made for every fifty (50) cubic meters of concrete but in no case less than one (1) test for each day’s concreting.

Samples shall be taken by the Contractor under close supervision of the Engineer, and shall be delivered as soon as practicable for testing, at his expense, to the designated laboratories.

The averages strength of test samples representing any definite class of concrete used as well as the average of any five (5) consecutive strength test representing the class of concrete shall be equal to or greater than the specified strength and not more than one (1) strength test in ten shall have an average value less than 90% of the specified strength.

If the test results indicate strength values less than the required, the General manager shall have the right to order a change in concrete proportion used for the remaining work, or in the procedures of curing the concrete.

## Liquidated Damages (Specific)

For failure to meet the specified strength required for concrete, designed, prepared and laid by him, the Contractor shall pay the AUTHORITY as liquidated damages, not as penalty or forfeiture the following to be applied only to the quantity of concrete which the particular sample/s represent.

Payment of 30% contract unit cost per cubic meter of concrete affected for test resulting to strength between 90 to 100 percent of specified strength;

Payment of 50% contract unit cost per cubic meter of concrete affected for test resulting to strength between 80 to 90 percent of specified strength;

Non-payment and removal and replacement at cost to the Contractor of all concrete affected for test resulting to strengths below 80 percent to that specified; provided that;

Field Tests

Field test as may be deemed necessary to check on the quantity of the materials and mixtures and the Project Engineer assigned to the project shall conduct the manner of construction employed. And when such tests results to values less than that tolerated by standards set in applicable provisions of the ASTM Specifications referred to herein, or contrary to accepted good engineering practice, the Contractor shall comply to any instructions given by the Project Engineer to upgrade the materials used and method of construction employed.

## Design and Manufacturing Specification Requirements:

Designated load capacity of mooring bitts shall be as shown on the drawings, and shall be referred to as the safe working load.  The mooring bitts shall be capable of withstanding a proof test load of 1.5 times the safe working load.

Mooring bitts shall be of the dimensions, weights, capacities and designs that are in accordance with shop drawings, approved by the Engineer and shall be fabricated by approved manufacturer with cast steel conforming to the requirements indicated in the plan/drawings, or approved equivalent.

The size of the bolts, nuts and washers shall be in accordance with the specifications provided in the plan/drawings. All bolts, nuts, washers etc., that are exposed shall be galvanized to the satisfaction of the Engineer.

Samples of bolts, nuts, washers and anchor plates shall be submitted to the Engineer for approval before being used in the Works.

## Concrete Foundation:

Concrete foundation for mooring bitts shall conform to the requirements of  “Reinforced Concrete”.

## Visual Inspection:

All mooring bitts delivered to the site shall be inspected by the Engineer for any signs of flaws or defect inimical to usage.

## Mill Test Certificates:

Two (2) copies of mill test reports shall be submitted certifying that materials meet the specified standards.

## Test Inspection:

Inspection of all materials and methods of fabrication shall be carried out by the Contractor.  However, the Engineer reserves the right to inspect all facilities at any time during manufacture to ensure that the materials and workmanship are in accordance with Specifications and the best of Workmanship.

STRUCTURAL STEEL WORKS

Materials shall conform to ASTM designation A36-700 or equivalent.  Shapes of structural members shall be as shown in the plans or in the AISC.  Steel less than 4.75 mm thick shall be in accordance with American Iron and Steel Institute’s Light Gauge Steel Design Specifications.  Materials and parts necessary to complete each item, even though such work is not definitely shown or specified shall be included.  Miscellaneous bolts, hinges, and braces supports and connections necessary for completion of the work shall be provided.

Where welds are used, either at works or on site, they are, whenever possible, to be continued and returned around any melting face to ensure that the joints are completely sealed against corrosion.  Electrodes for Arc Welding shall conform to America Welding Society Specifications.  Surfaces to be welded shall be free from loose scale, slag, rust, grease, paint and any other foreign materials except that Mill Scale, which withstands vigorous wire brushing, may remain.

Parts to be fillet welded shall be brought in as close contact as practicable in no event shall be separated by more than 4.75 mm.

The technique of welding employed, the appearance and quality of welds made, and the methods used in correcting defective work shall conform to Section 4 – Workmanship, of the STANDARD CODE FOR ARC GAS WELDING IN BUILDING CONSTRUCTION of the American Welding Society.

ELECTRICAL WORKS

Scope of Work:

The Work to be done shall consist of the fabrication, trenching, furnishing, delivery and installation of electrical materials. Complete all details of electrical works as shown in the drawings including materials, labor, tools and equipment, and all incidental work necessary to complete the installation of all electrical works.

Refer to electrical plans/drawings for location and extent of work involved.

General Requirements

All works shall be done in accordance with the requirements of the government agencies having jurisdictions as well as the requirements of the following:

1. National Fire Protection Association		-		(NFPA)

2. National Electrical Manufacturer’s Association	-		(NEMA)

3. Underwriter’s Laboratories, Inc.			-		(UL)

4. Philippine Electrical Code 			- 		(PEC)

5. Philippine National Standard			-		(PNS)

Unless otherwise specified, the materials and equipment to be furnished shall be standard products of reputable manufacturer engaged in the production of such materials and equipment.

The Contractor shall submit for approval the samples of lighting fixtures specified or shown on the plans.

Materials Requirement

All electrical materials and equipment for the area lighting shall be furnished and installed by the contractor.

Execution

The Contractor shall furnish and install lighting fixtures complete for all lighting outlets as shown on drawings.

All materials and fixtures accessories, whether specifically described or not, shall be of the best grace.

All lighting fixtures shall be complete with lamps, lamp auxiliaries, support appurtenances, etc., as part of the electric work, unless otherwise noted. Lighting fixtures shall in all cases be suitable for the voltage of the circuits to which they are being applied.

Wiring

Internal wiring of fixtures shall contain a minimum number of species. All splices shall be made with approved insulated expandable coil steel spring “wire unit” type mechanical connectors, suitable for the temperature and voltage conditions the splices are subjected to within the fixtures

Fixture Mounting

The exact location of height of the fixture shall be as indicated and shall be as shown on the drawings.

Workmanship

The work throughout shall be executed in the best and most thorough manner under the direction of the Engineer,  who will interpret the intent meaning of the drawings and specifications and shall have the power to reject any work and materials which in his judgment are not in full accordance therewith.

Testing Operations

When the area lighting installation is completed, the Contractor shall test the wiring and equipment operation in the presence of the Engineer. The system shall be free from any defects, shorts or grounds. All necessary instruments and personnel required for the testing shall be furnished by the Contractor at no extra cost to the Authority.

Guarantee

Upon completion and before final acceptance of the work, the contractor shall furnish the Engineer a written guarantee stating that all works executed are free from defects on materials and workmanship. The guarantee shall be a period of one year for the date of final acceptance. Any work that becomes defective during the period shall be replaced by the Contractor at his own expense in a manner satisfactory to the Authority.

As-Built Drawings

Upon completion and before final acceptance of work the Contractor shall prepare at his own expense and submit to the Engineer as-built drawings incorporating all approved changes, omissions and/or addition to the contract drawings, three printed copies of as-built drawings together with their reproducible originals at no extra cost to the Authority.

Where as-built drawing is required for submission to enforcing Authorities, same shall be submitted first to the Engineer for verification and checking. One set of the drawings shall be duly approved by the proper enforcing Authorities shall be submitted together with the reproducible originals.

ROOFINGS

Coloroof, 0.40mm x 1020mm x 6000mm rib-type roofing shall be provided for the whole roofing requirements of the structure.  The roofing shall be fastened by Tex Screw including necessary fittings and caps to provide completely sound and watertight roofs.

Ridge Rolls, Flashings and Gutters shall be pre-painted/pre-fab/bended Coloroof installed in accordance with the drawings/plans.

CARPENTRY, FALSEWORKS AND FORM WORKS

Falsework shall be set to provide the required camber and to compensate for deadlock deflection when the falsework is removed.  Forms shall be filleted at all sharp corners and leveled to insure easy removal.  All forms shall be treated with oil or other materials prior to pouring to lessen adherence of the concrete to the forms.

Wooden materials shall be of good quality, well seasoned, thoroughly dry and free from loose or unsound knots, shakes or other imperfections impairing their strength or appearances.  The kind of lumber to be used  for the various parts of the building shall be  apitong or laua-an for second floor framings, trusses, purlins, fascia board, ceiling joists, vertical and horizontal studs of partition walls,  stair treads, stringer, risers and handrails, and yacal for door and window jambs.

Doors and doorframes shall conform to the sizes, designs and kind of materials shown in the details and schedule of doors and windows.

All wood frames/jambs for doors shall be done as much as possible, with carefully fitted mortise and tenon joints.

Steel windows to be used in this project shall conform to the size and design shown in the plans.

PAINTING WORKS

General

The work included in this section consists of the furnishing of all labor, materials, tools and all appurtenant work in connection with painting and coatings in accordance with these specifications. All paints and coatings shall be applied by painting subcontractors and workmen approved by the Engineer.

##### Scope

The following surfaces are to be painted expect where otherwise specified or shown:

- Metal surfaces and above ground piping

- All exposed concrete

- All structural and miscellaneous metal

- All equipment furnished without factory finished surfaces

- All exposed steel mullions, tubular f4rames, door frames, steel sash and metal windows

- All sheet metal and ferrous metal trim.

- Interior and exterior surfaces of the building including all concrete block masonry

The following surfaces are not to be painted:

- Ferrous metals having approved plating or factory paint finishes.

- Non-ferrous metals, unless otherwise specified of indicated; galvanized metal shall not be considered a non-ferrous metal.

- Equipment with factory finished surfaces unless otherwise specified.

No concrete, wood metal or any other surfaces requiring protection shall be left unpainted even not specifically defined herein.

Ferrous metals without approved plating or factory paint finishes shall be protected against rust and corrosion from effects of salt water, high humidity and contaminating influences of pitting, scaling and weakening.

Right of Rejection

Exterior painting or interior finishing shall be done under conditions which shall not jeopardize the appearance or quality of the painting of finishing in any way. The Engineer shall have the right to reject all materials or work in the course of the painting job.

Protection of the Work

The contractor shall endeavor to protect the work of others during the time painting work is in progress. The contractor shall be responsible for any and all damage to any other work in the course of the painting job.

Protective coverings shall be used to protect floors, fixtures and equipment while painting. Care shall be exercised to prevent paint being spattered onto surfaces which are not to be painted.

Workmanship

All painting work shall be first class and in accordance with the best standard practices of the trade.

The contractor shall examine carefully al surfaces to be painted and before beginning any work, shall make sure that the work of other trades has been installed in s\a workman like condition ready to receive paint.

Metal surfaces shall be applied with a solution to make it clean, dry and free from mill scale, rust, grease, oil or any other substances before applying (spraying or brush) in concentrated form a solution that will retard the effects of salt water and other brine salts, such as sodium chloride (NaCi), calcium chloride (CaCi) and zinc bromide (ZnBr) which could affect the quality of structural steel-ferrous metals before the application of paint primer solution and metal finish coating.

Paint shall be applied in the right consistency and each coat shall be brushed evenly free of brush marks, sags and runs. Care shall be exercised to avoid lapping of paint on glass or hardware. Paint shall be sharply applied to required lines. Finished paint surfaces shall be free from defects or blemishes. Surfaces from which such paint cannot be removed satisfactorily shall be painted or repainted, as required to produce a finish satisfactory to the Engineer.

Succeeding paint coatings shall be applied only when the previous coat is hard and dry.

All painting materials shall be used strictly in accordance with the manufacturer’s directions.

Storage of Materials

All painting materials and equipment not for immediate use shall be stored in a room approved by the Engineer for that purpose. The receiving, opening and mixing of all paint materials shall be done in this room.

Necessary precautions shall be taken to prevent fire. Rags, waste and other materials, soiled with paint shall be removed from the premises at the end each day’s work or stored in metal containers with metal covers.

Preparation of Paint

Paint containers shall be delivered to be the job site in manufacturer’s unopened containers and shall be opened only when required for use. Paint shall be mixed only in the designated room or space in the presence of the Engineer or his representative. Paint shall be thoroughly stirred or agitated to uniformly smooth consistency suitable for proper application. Unless otherwise specified or approved, no materials shall be reduced, changed or used except in accordance with manufacturer’s label or tag on container. In all cases, paint shall be prepared and handled in manner that will prevent deteriorated and contamination with pollutants.

Clean-Up

Upon completion of work, the Contractor shall remove all surplus material. All paint spills shall be removed and the entire premises shall be cleaned of all rubbish, and debris, caused by the work. Finished surfaces shall be presented clean and free from blemishes and is acceptable in every way. Al glass shall be4 cleaned of paint spots and polished before the job is presented for acceptance by the owner.

Materials

a) Materials	-	A complete list of materials proposed for use shall be submitted by the Contractor for the Engineer’s approval. The Contractor may substitute other paint materials for those specified in section 27.12 provided written approval from the Engineer is received stating that said proposed substitute materials are equal to that specified and are approved for use. The painting material shall be delivered to the job site in its original containers properly labeled without evidence of tampering, substitution of contents, or of deterioration.

b) Color and Sample	- 	all finish colors shall be as selected by the Owner. In multicoat work using color pigmented paints, each coat shall have sufficient variation of color to easily distinguish it from the preceding coat.

Using specified or approved materials, 3 sample panels of each finish, including all coats thereof shall be prepared and submitted for the Owner’s approval. Complete work shall match approved colors and samples.

Preparation of Surfaces

a) General	-	except as otherwise specified, surfaces to be painted shall be clean, smooth and dry. The Contractor shall report to the Engineer in writing any surfaces which cannot be properly prepared for painting if work is commenced before defects have been reported and corrected, any resulting unsatisfactorily finish shall be rectified at no cost to the PPA.

b) Concrete and Masonry 	-	All concrete and masonry surfaces shall be cured thirty day prior to painting. Dirt, dust, oil, grease efflorescence and other deleterious matter shall be removed and surfaces roughed when necessary to insure good paint adhesion. The method of surface preparation shall be left to the discretion of the Contractor, but results obtained shall be satisfactory to the Engineer. Before application of resin emulsion paint, surfaces shall be prepared in accordance with the manufacturer’s directions. Before application of oil base or latex paints, surfaces shall be tested for presence of alkali; if alkali is present, neutralize as recommended by the manufacturer of the pain materials to be applied.

c) Plaster	-	Dirt, dust, loose plaster and other deleterious matter which would prevent good paint adhesion shall be removed. All holes, cracks and depression shall be neatly filled with patching plaster, mixed and applied to match existing plaster. Patches shall be sanded flush and smooth and properly sealed before applying prime coat. After priming surfaces, suction spots shall be touched up with additional prime coat material until surfaces evidence a uniform coating. Enamel undercoats on smooth plaster shall be sandpapered by hand (with no.00 sandpaper) and dusted clean before applying succeeding.

d) Metal	-	Dirt, scale and rust shall be removed by scraping, wire brushing and sanding or sandblasting as required. Oil and grease shall be removed with mineral spirits or appropriate solvent. Before painting ferrous metal surfaces, including galvanized ferrous metal, surfaces shall be pretreated with approved phosphoric acid etching cleaner in accordance with the manufacturer’s directions to produce a chemically clean surface. Unless already performed in accordance with specifications of other sections, abrasions and bare spots in shop prime coatings shall be touched up with metal prime matching the shop coatings. Enamel undercoats shall be sandpapered by hand (with no.00 sandpaper) and dusted clean before applying succeeding coat.

e) Woodwork	-	Unless already properly sanded, woodwork shall be sandpapered smooth by hand before priming surfaces, knots, pitch pockets and sap steaks shall be thoroughly cleaned of residue and touched up with shellac varnish coating. After priming surface, nail holes, cracks and depressions shall be neatly filled with putty or other approved filler, colored to match required finish. Enamel undercoats shall be sanded by sand (with no.00 sandpaper) and dusted clean before applying succeeding coat.

Application of Paint

a) General	-	All painting and finishing shall be performed by skilled craftsmen. Each coat of paint shall be applied with the right consistency, evenly, free of laps, sags and runs and cut sharply to required lines. Paint shall be applied only under dry and dust free conditions that will insure properly finished surfaces, free of defects and blemishes unless otherwise directed by the Engineer. Paint shall not be applied when temperature is likely to be above 90 F. sufficient time shall be allowed between applications of coats. All primer and intermediate coats shall be unscarred and completely integral at time of application of each succeeding coat. The Engineer shall be notified when each coat is inspected and approved by the Engineer, no succeeding coats shall be applied. Whenever he coats of a dark colored paint are specified the first coat shall contain sufficient powdered aluminum t act as an indicator for proper coverage when applying the second coat.

b) Method of Application	-	Paint should be applied by brush, spray, or other application method approved by the Engineer.

c) Priming and Back Painting

Priming	-	Before installation, all surfaces of millwork which are to be painted shall be primed giving particular attention to sealing of cross grained surfaces. In all cases, all work shall be primed as soon as possible after installation, as required, or in case of prefabricated items, at fabricator’s shop or mill before shipment, if practicable. Except as otherwise specified, priming shall consists of first coat herein after specified under “ Finishes”.

Back-Painting	-	woodwork, millwork and casework to be installed against concrete masonry or plaster shall be back painted with one.

# Section VII. Drawings

Insert here a list of Drawings.  The actual Drawings, including site plans, should be attached to this section or annexed in a separate folder.

# Section VIII. Bill of Quantities

Notes on the Bill of Quantities Objectives The objectives of the Bill of Quantities are: (a) to provide sufficient information on the quantities of Works to be performed to enable Bids to be prepared efficiently and accurately; and (b) when a Contract has been entered into, to provide a priced Bill of Quantities for use in the periodic valuation of Works executed. In order to attain these objectives, Works should be itemized in the Bill of Quantities in sufficient detail to distinguish between the different classes of Works, or between Works of the same nature carried out in different locations or in other circumstances which may give rise to different considerations of cost. Consistent with these requirements, the layout and content of the Bill of Quantities should be as simple and brief as possible. Daywork Schedule A Daywork Schedule should be included only if the probability of unforeseen work, outside the items included in the Bill of Quantities, is high. To facilitate checking by the Entity of the realism of rates quoted by the Bidders, the Daywork Schedule should normally comprise the following: (a) A list of the various classes of labor, materials, and Constructional Plant for which basic daywork rates or prices are to be inserted by the Bidder, together with a statement of the conditions under which the Contractor will be paid for work executed on a daywork basis. (b) Nominal quantities for each item of Daywork, to be priced by each Bidder at Daywork rates as Bid. The rate to be entered by the Bidder against each basic Daywork item should include the Contractor’s profit, overheads, supervision, and other charges. Provisional Sums A general provision for physical contingencies (quantity overruns) may be made by including a provisional sum in the Summary Bill of Quantities. Similarly, a contingency allowance for possible price increases should be provided as a provisional sum in the Summary Bill of Quantities. The inclusion of such provisional sums often facilitates budgetary approval by avoiding the need to request periodic supplementary approvals as the future need arises. Where such provisional sums or contingency allowances are used, the SCC should state the manner in which they will be used, and under whose authority (usually the Procuring Entity’s Representative’s). The estimated cost of specialized work to be carried out, or of special goods to be supplied, by other contractors (refer to GCC Clause 8) should be indicated in the relevant part of the Bill of Quantities as a particular provisional sum with an appropriate brief description. A separate procurement procedure is normally carried out by the Procuring Entity to select such specialized contractors. To provide an element of competition among the Bidders in respect of any facilities, amenities, attendance, etc., to be provided by the successful Bidder as prime Contractor for the use and convenience of the specialist contractors, each related provisional sum should be followed by an item in the Bill of Quantities inviting the Bidder to quote a sum for such amenities, facilities, attendance, etc. Signature Box A signature box shall be added at the bottom of each page of the Bill of Quantities where the authorized representative of the Bidder shall affix his signature. Failure of the authorized representative to sign each and every page of the Bill of Quantities shall be a cause for rejection of his bid. These Notes for Preparing a Bill of Quantities are intended only as information for the Procuring Entity or the person drafting the Bidding Documents. They should not be included in the final documents.

| BILL OF QUANTITIES |
| --- |
| Project Title/Code : REPAIR OF PASSENGER TERMINAL BUILDING AT PORT OF ESTANCIA, ILOILO Project Location : Brgy.Botongon,Estancia,Iloilo |
| ITEM / BILL | DESCRIPTION OF WORK | UNIT | QTY. | UNIT PRICE | AMOUNT |
| No. |  |  |  | (PhP) | (PhP) |
| (1) | (2) | (3) | (4) | (5) | (4) x (5) |
| 1.00 | Mobilization/ Demobilization | lot | 1 |  |  |
| 2.00 | Removal of Vinyl Floor Tiles | sq.m | 431.25 |  |  |
| 3.00 | Installation of Floor Tiles |  |  |  |  |
| 3.01 | Supply, Deliver and Install Floor Tiles (Ground Floor) | sq.m | 197.50 |  |  |
| 3.02 | Supply, Deliver and Install Floor Tiles ( 2nd Floor ) | sq.m | 233.75 |  |  |
| 3.03 | Supply, Deliver and Install Floor Tiles(Stair) | sq.m | 16.75 |  |  |
| 4.00 | Demolition, Disposal of old wooden partition & Construction of new partitions |  |  |  |  |
| 4.01 | Remove & dispose of old wooden partition to designated area directed by engineer. | sq.m | 175.00 |  |  |
| 4.02 | Fabrication of wooden Partition and installation of glass partition incdg.finishing | sq.m | 146.83 |  |  |
| 4.03 | Surface Preparation, Prime and Final Painting of Doors & Item 4.02. | sq.m | 615.22 |  |  |
| 5.00 | Repair of PTB Ceiling |  |  |  |  |
| 5.01 | Removal and dispose of existing ceiling incdg stockpiling to designated area. | sq.m | 431.25 |  |  |
| 5.02 | Supply, Deliver and Install of Ceiling including joist and boards (Ground & 2nd Floor) | sq.m | 432.18 |  |  |
| 6.00 | Remove, Dispose and Install Doors & Windows |  |  |  |  |
| 6.01 | Remove & dispose of old doors & windows to designated site | sq.m | 110.10 |  |  |
| 6.02 | Supply/Deliver and Install new set of Doors(10sets) and Windows(27) | sq.m. | 110.10 |  |  |
| 6.03 | Leveling/Finishing of Windows/ Door Sill | cu.m | 263.00 |  |  |
| 6.04 | Painting of Doors | sq.m | 59.56 |  |  |
| 7.00 | Repair of PTB Roofing’s |  |  |  |  |
| 7.01 | Removal and Disposal of old Corr.G.I Sheets and other accessories | sq.m. | 313.90 |  |  |
| 7.02 | Supply,Deliver and Install of new Roofing and accessories. | sq.m. | 313.90 |  |  |
| 8.00 | Paintings of Concrete Walls (Interior & Exterior),Parapet wall, wooden Partitions | sq.m. | 2,174.23 |  |  |
| 9.00 | Electricals |  |  |  |  |
| 9.01 | Fixtures and Receptacles | lot | 1.00 |  |  |
| 9.02 | Power Panels & Service Equipment | lot | 1.00 |  |  |

# Section IX. Bidding Forms

TABLE OF CONTENTS

Bid Form	104

Form of Contract Agreement	106

Omnibus Sworn Statement	108

Bid Securing Declaration………………………………………………………91

#### Bid Form

Date:

IB No:

To:  [name and address of PROCURING ENTITY]

Address: [insert address]

We, the undersigned, declare that:

- We have examined and have no reservation to the Bidding Documents, including Addenda, for the Contract [insert name of contract];

- We offer to execute the Works for this Contract in accordance with the Bid and Bid Data Sheet, General and Special Conditions of Contract accompanying this Bid;

The total price of our Bid, excluding any discounts offered below is: [insert information];

The discounts offered and the methodology for their application are: [insert information];

- Our Bid shall be valid for a period of [insert number] days from the date fixed for the Bid submission deadline in accordance with the Bidding Documents, and it shall remain binding upon us and may be accepted at any time before the expiration of that period;

- If our Bid is accepted, we commit to obtain a Performance Security in the amount of  [insert percentage amount] percent of the Contract Price for the due performance of the Contract;

- Our firm, including any subcontractors or suppliers for any part of the Contract, have nationalities from the following eligible countries: [insert information];

- We are not participating, as Bidders, in more than one Bid in this bidding process, other than alternative offers in accordance with the Bidding Documents;

- Our firm, its affiliates or subsidiaries, including any subcontractors or suppliers for any part of the Contract, has not been declared ineligible by the Funding Source;

- We understand that this Bid, together with your written acceptance thereof included in your notification of award, shall constitute a binding contract between us, until a formal Contract is prepared and executed; and

- We understand that you are not bound to accept the Lowest Calculated Bid or any other Bid that you may receive.

- We likewise certify/confirm that the undersigned, is the duly authorized representative of the bidder, and granted full power and authority to do, execute and perform any and all acts necessary to participate, submit the bid, and to sign and execute the ensuing contract for the [Name of Project] of the [Name of the Procuring Entity].

- We acknowledge that failure to sign each and every page of this Bid Form, including the Bill of Quantities, shall be a ground for the rejection of our bid.

Name:

In the capacity of:

Signed:

Duly authorized to sign the Bid for and on behalf of:

Date: 	___________

#### Form of Contract Agreement

THIS AGREEMENT, made this [insert date] day of [insert month], [insert year] between [name and address of PROCURING ENTITY] (hereinafter called the“Entity”) and [name and address of Contractor] (hereinafter called the “Contractor”).

WHEREAS, the Entity is desirous that the Contractor execute [name and identification number of contract] (hereinafter called “the Works”) and the Entity has accepted the Bid for [insert the amount in specified currency in numbers and words] by the Contractor for the execution and completion of such Works and the remedying of any defects therein.

NOW THIS AGREEMENT WITNESSETH AS FOLLOWS:

            - In this Agreement, words and expressions shall have the same meanings as are respectively assigned to them in the Conditions of Contract hereinafter referred to.

- The following documents shall be attached, deemed to form, and be read and construed as integral part of this Agreement, to wit:

  - General and Special Conditions of Contract;

  - Drawings/Plans;

  - Specifications;

  - Invitation to Bid;

  - Instructions to Bidders;

  - Bid Data Sheet;

  - Addenda and/or Supplemental/Bid Bulletins, if any;

  - Bid form, including all the documents/statements contained in the Bidder’s bidding envelopes, as annexes, and all other documents submitted (e.g., Bidder’s response to request for clarifications on the bid), including corrections to the bid, if any, resulting from the Procuring Entity’s bid evaluation;

  - Eligibility requirements, documents and/or statements;

  - Performance Security;

  - Notice of Award of Contract and the Bidder’s conforme thereto;

  - Other contract documents that may be required by existing laws and/or the Entity.

- In consideration of the payments to be made by the Entity to the Contractor as hereinafter mentioned, the Contractor hereby covenants with the Entity to execute and complete the Works and remedy any defects therein in conformity with the provisions of this Contract in all respects.

- The Entity hereby covenants to pay the Contractor in consideration of the execution and completion of the Works and the remedying of defects wherein, the Contract Price or such other sum as may become payable under the provisions of this Contract at the times and in the manner prescribed by this Contract.

IN WITNESS whereof the parties thereto have caused this Agreement to be executed the day and year first before written.

Signed, sealed, delivered by 	the 	 (for the Entity)

Signed, sealed, delivered by 	the 	(for the Contractor).

Binding Signature of Procuring Entity

________________________________________________

Binding Signature of Contractor

_____________________________________________

[Addendum showing the corrections, if any, made during the Bid evaluation should be attached with this agreement]

#### Omnibus Sworn Statement

REPUBLIC OF THE PHILIPPINES	)

CITY/MUNICIPALITY OF ______	) S.S.

AFFIDAVIT

I,   [Name of Affiant], of legal age, [Civil Status], [Nationality], and residing at [Address of Affiant], after having been duly sworn in accordance with law, do hereby depose and state that:

- Select one, delete the other:

If a sole proprietorship: I am the sole proprietor or authorized representative of [Name of Bidder] with office address at [address of Bidder];

If a partnership, corporation, cooperative, or joint venture: I am the duly authorized and designated representative of [Name of Bidder] with office address at [address of Bidder];

- Select one, delete the other:

If a sole proprietorship: As the owner and sole proprietor or authorized representative of [Name of Bidder], I have full power and authority to do, execute and perform any and all acts necessary to participate, submit the bid, and to sign and execute the ensuing contract for [Name of the Project] of the [Name of the Procuring Entity] [insert “as shown in the attached duly notarized Special Power of Attorney” for the authorized representative];

If a partnership, corporation, cooperative, or joint venture: I am granted full power and authority to do, execute and perform any and all acts necessary to participate, submit the bid, and to sign and execute the ensuing contract for [Name of the Project] of the [Name of the Procuring Entity], accompanied by the duly notarized Special Power of Attorney, Board/Partnership Resolution, or Secretary’s Certificate, whichever is applicable;

- [Name of Bidder] is not “blacklisted” or barred from bidding by the Government of the Philippines or any of its agencies, offices, corporations, or Local Government Units, foreign government/foreign or international financing institution whose blacklisting rules have been recognized by the Government Procurement Policy Board;

- Each of the documents submitted in satisfaction of the bidding requirements is an authentic copy of the original, complete, and all statements and information provided therein are true and correct;

- [Name of Bidder] is authorizing the Head of the Procuring Entity or its duly authorized representative(s) to verify all the documents submitted;

- Select one, delete the rest:

If a sole proprietorship: The owner or sole proprietor is not related to the Head of the Procuring Entity, members of the Bids and Awards Committee (BAC), the Technical Working Group, and the BAC Secretariat, the head of the Project Management Office or the end-user unit, and the project consultants by consanguinity or affinity up to the third civil degree;

If a partnership or cooperative: None of the officers and members of [Name of Bidder] is related to the Head of the Procuring Entity, members of the Bids and Awards Committee (BAC), the Technical Working Group, and the BAC Secretariat, the head of the Project Management Office or the end-user unit, and the project consultants by consanguinity or affinity up to the third civil degree;

If a corporation or joint venture: None of the officers, directors, and controlling stockholders of [Name of Bidder] is related to the Head of the Procuring Entity, members of the Bids and Awards Committee (BAC), the Technical Working Group, and the BAC Secretariat, the head of the Project Management Office or the end-user unit, and the project consultants by consanguinity or affinity up to the third civil degree;

- [Name of Bidder] complies with existing labor laws and standards; and

- [Name of Bidder] is aware of and has undertaken the following responsibilities as a Bidder:

  - Carefully examine all of the Bidding Documents;

  - Acknowledge all conditions, local or otherwise, affecting the implementation of the Contract;

  - Made an estimate of the facilities available and needed for the contract to be bid, if any; and

  - Inquire or secure Supplemental/Bid Bulletin(s) issued for the [Name of the Project].

- [Name of Bidder] did not give or pay directly or indirectly, any commission, amount, fee, or any form of consideration, pecuniary or otherwise, to any person or official, personnel or representative of the government in relation to any procurement project or activity.

IN WITNESS WHEREOF, I have hereunto set my hand this __ day of ___, 20__ at ____________, Philippines.

_____________________________________

Bidder’s Representative/Authorized Signatory

SUBSCRIBED AND SWORN to before me this ___ day of [month] [year] at [place of execution], Philippines. Affiant/s is/are personally known to me and was/were identified by me through competent evidence of identity as defined in the 2004 Rules on Notarial Practice (A.M. No. 02-8-13-SC). Affiant/s exhibited to me his/her [insert type of government identification card used], with his/her photograph and signature appearing thereon, with no. ________ and his/her Community Tax Certificate No. _______ issued on ____ at ______.

Witness my hand and seal this ___ day of [month] [year].

NAME OF NOTARY PUBLIC

Serial No. of Commission _______________

Notary Public for _______ until __________

Roll of Attorneys No. __________________

PTR No. ______ [date issued], [place issued]

IBP No. ______  [date issued], [place issued]

Doc. No. _____

Page No. _____

Book No. _____

Series of _____

* This form will not apply for WB funded projects.

Bid-Securing Declaration

(REPUBLIC OF THE PHILIPPINES)

CITY OF _______________________ ) S.S.

x-------------------------------------------------------x

Invitation to Bid  [Insert reference number]

To: [Insert name and address of the Procuring Entity]

I/We, the undersigned, declare that:

            - I/We understand that, according to your conditions, bids must be supported by a Bid Security, which may be in the form of a Bid-Securing Declaration.

            - I/We accept that: (a) I/we will be automatically disqualified from bidding for any contract with any procuring entity for a period of two (2) years upon receipt of your Blacklisting Order; and, (b) I/we will pay the applicable fine provided under Section 6 of the Guidelines on the Use of Bid Securing Declaration, within fifteen (15) days from receipt of written demand by the procuring entity for the commission of acts resulting to the enforcement of the bid securing declaration under Sections 23.1(b), 34.2, 40.1 and 69.1, except 69.1 (f), of the IRR of RA 9184; without prejudice to other legal action the government may undertake.

            - I/We understand that this Bid-Securing Declaration shall cease to be valid on the following circumstances:

              - Upon expiration of the bid validity period, or any extension thereof pursuant to your request;

              - I am/we are declared ineligible or post-disqualified upon receipt of your notice to such effect, and (i) I/we failed to timely file a request for reconsideration or (ii) I/we filed a waiver to avail of said right;

              - I am/we are declared as the bidder with the Lowest Calculated Responsive Bid, and I/we have furnished the performance security and signed the Contract.

IN WITNESS WHEREOF, I/We have hereunto set my/our hand/s this ____ day of [month] [year] at [place of execution].

[Insert NAME OF BIDDER’S AUTHORIZED REPRESENTATIVE]

[Insert signatory’s legal capacity]

Affiant

SUBSCRIBED AND SWORN to before me this __ day of [month] [year] at [place of execution], Philippines. Affiant/s is/are personally known to me and was/were identified by me through competent evidence of identity as defined in the 2004 Rules on Notarial Practice (A.M. No. 02-8-13-SC). Affiant/s exhibited to me his/her [insert type of government identification card used], with his/her photograph and signature appearing thereon, with no. ______.

Witness my hand and seal this ___ day of [month] [year].

NAME OF NOTARY PUBLIC

Serial No. of Commission ___________

Notary Public for ______ until _______

Roll of Attorneys No. _____

PTR No. __, [date issued], [place issued]

IBP No. __, [date issued], [place issued]

Doc. No. ___

Page No. ___

Book No. ___

Series of ____.

# Footnotes

Unless the Treaty or International or Executive Agreement expressly provides use of foreign government/foreign or international financing institution procurement guidelines.

Two years after the effectivity of the 2016 Revised IRR of RA 9184 on 28 October 2016, advertisement in a newspaper of general nationwide circulation shall no longer be required. However, a Procuring Entity that cannot post its opportunities in the PhilGEPS for justifiable reasons shall continue to publish its advertisements in a newspaper of general nationwide circulation.

If ADB, JICA and WB funded projects, use IFB.